## Slide 1: Understanding Performance Metrics of Processors
Bina Ramamurthy
Chapter 1

## Slide 2: Performance
Section 1.4 onwards
Performance, relative performance, measuring performance, program performance, CPU performance, instruction performance
Using the performance equation
Classic CPU performance equation
Power wall
Transition from uniprocessor to multi-processor
SPEC (System Performance Evaluation Cooperative) benchmark

## Slide 3: How do you define performance?
For airplanes:
  Is this the highest cruising speed?
  Is the the longest range?
  Is this the largest capacity?
  Others….see table 1.13
Processor performance of a processor
Perf= 1/ ExTime
PerfX > PerfY implies ExTimeX < ExTimeY
n = PerfX / PerfY means processor X is n times faster than processor Y
Lets look at an example.

## Slide 4: Relative Performance Example
If a computer A runs a program in 10 secs and a computer B runs the program in 15 secs, how much faster is A than B?
N = PerfA/PerfB = ExTimeB/ ExTimeA = 15/10 = 1.5

## Slide 5: Measuring Performance
CPU execution time is measured in clock cycles
Clock cycles time or period depends on clock rate (cycles/sec)
CPU Ex time =
  CPU clock cycles for the program X clock cycle time
CPU Ex time =
  CPU clock cycles for a program / clock rate

## Slide 6: Example: Improving Performance
A program runs in 10 secs on processor A with 2Ghz clock.
We want to design a processor B which will run this program in 6 secs.
The change of design in processor B results in 1.2 times as many clock cycles as processor A.
Lets work out this problem and find out the clock rate of the processor B.

## Slide 7: Instruction Performance (CPI)
How do you determine CPU cycles for a program?
CPU cycles for a program =
# instructions for the program X average clock cycles per instruction
= #instruction X CPI
CPI provides another way of comparing two different implementations of the same ISA (instruction set architecture)

## Slide 8: CPI Example
Consider two different implementations of the same ISA. Processor A has a clock cycle time of 250ps and a CPI of 2.0 for some program.
Processor B has a clock cycle time of 500ps and a CPI of 1.2 for the same program.
Which is faster for this program and by how much?

## Slide 9: Classic CPU Performance Equation
CPU time=
instruction count X CPI X Clock cycle time
CPU time = Instruction count X CPI /clock rate
Importance of this equation is that it separates three key factors that affect performance.
Lets look at an example on page 35.

## Slide 10: Example: CPU time with instruction set
Consider the CPI for three classes of instructions of a processor:
CPI for class A, B and C instruction is 1, 2 and 3 respectively
Code sequence one has {2, 1, 2} of {A, B, C} class of instructions
Code sequence two has {4, 1, 1} of {A, B, C} class of instructions
Which code sequence executes the most instructions? Which will be faster? What is the CPI for each sequence?

## Slide 11: Components of performance and how each is measured
Component | Units of measure
CPU execution time for a program | seconds
Instruction count | # of instructions
CPI(clock cycles per instruction) | Average# clock cycles / inst
Clock cycle time | seconds

## Slide 12: Dependency of Performance
Performance depends of
Algorithm
Programming language
Compiler
Instruction set architecture (ISA)
Final example on p.38