## Slide 1: Embedded XINU SW & HW preparation
09/5/2008
David You

## Slide 2: Software preparation
Download the Embedded XINU ver 1.0
Cross-compiler
  A cross-compiler from a host computer's architecture to MIPSEL (little endian MIPS)
  http://xinu.mscs.mu.edu/HOWTO:Build_and_Deploy_XINU
Serial communication software
TFTP server software (30-day Trial version)
  http://www.tftp-server.com/tftp-download.html

## Slide 3: Hardware preparation
Modified WRT54GL router
  http://xinu.mscs.mu.edu/HOWTO:Modify_the_Linksys_hardware
Computer(s)
  Run TFTP server
  Compile the XINU with cross compiler
  Connect the router trough the serial communication
An extra router
  Establishing a small network between a computer and the modified router for downloading the XINU onto the router.

## Slide 4: Connection
Network connection
Serial Communication
IP: 192.168.0.130
IP: 192.168.0.101

## Slide 5: How to download XINU onto the router?
http://xinu.mscs.mu.edu/HOWTO:Connect_to_a_modified_router
Check the connection among the devices.
Check the IP address given by the D-link router to the computer.
Run a TFTP server program and put the XINU boot image in a proper directory.
Make serial connection
  8 data bits, no parity bit, and 1 stop bit (8N1), 115200 bps.
Get the CFE prompt
  First, push the CTRL+C with the serial connection open and then power on the WRT54GL.
Change the IP address of the network
  CFE> ifconfig eth0 -auto
Download the boot image
  CFE> boot -elf [TFTP server IP]:xinu.boot