CSE321 Homework 2  Due date: 10/6/2009 in class.

1. (20 points) Real-time Scheduling :  Rate Monotonic Scheduling (RMS)

Use the RMS schedulability analysis to check if each of the following task sets is schedulable with RMS. If not, draw a timing chart to show where the first deadline miss occurs.

| Task Set |
| --- |
| Task | Period | Execution time |
| 1 | 5 | 1 |
| 2 | 7 | 2 |
| 3 | 9 | 4 |

2. (20 points) Real-time Scheduling: Earliest Deadline Scheduling (EDS)

For the same task set given in Question 1 use the EDS schedulability analysis to check if each of the following task sets is schedulable with EDS. Draw the timing chart for at least two cycles of each task.