## Slide 1: Introduction to Xinu and Kernel Programming
Bina Ramamurthy
bina@buffalo.edu

## Slide 2: Embedded XINU and WRT54GL

## Slide 3: WRT54GL
History of WRT54G Open source firmware
Common features
Processor architecture (BCM5352)
WRT54GL Block diagram

## Slide 4: History
Introduced in 2002
The GNU General Public License (GNU GPL or GPL) is a widely used free software license, which guarantees end users (individuals, organizations, companies) the freedoms to run, study, share (copy), and modify the software.
The GNU General Public License does not permit incorporating your program into proprietary programs.
Read about Open Source movement.
In 2003 Andrew Miklas posted to Linux Kernel Mailing List about Linksys using GPL code in its firmware
Linksys executives gave into the pressure from the community, Linksys released the code to the community under GPL.

## Slide 5: Topics
WRT54GL architecture and internals
What is Xinu? And Embedded Xinu?
What is CFE?
Modifying WRT54GL to host Xinu: or port Xinu to MIPS platform
Connecting, compiling and deploying
Embedded Xinu Code reverse engineering

## Slide 7: Common Features
Power: 12VDC 1.0amp
  This power requirement is standard for embedded devices and wireless access points
  This makes them compatible with Power over Ethernet (PoE)
  This especially significant in mobile environment.
The Reset button: to reset the configuration

## Slide 8: Common Features (Contd.)
LED lights to indicate various conditions
Power : indicates presence of power
DMZ: use differs; ex: can show boot progress
WLAN LED
Ethernet
Internet
You can manipulate the LED thru’ your code by changing contents of system files.

## Slide 9: Linksys WRT54GL (contd.)
Linux kernel 2.4
Based on Broadcom BCM535E SoC (System on Chip)
All-in-one Internet-sharing router,
  4-port switch
  54Mbps wireless-G (802.11g) access point
  Shares a single internet connection with Ethernet wired and wireless-G –B devices
  Push button setup
  High security: TKIP and AES encryption providing a powerful firewall

## Slide 10: Processor Architecture
WRT54Gl uses Broadcom MIPS (Microprocessor without Interlocked Pipelines Stages) processor, common to embedded devices and game consoles.
Model: BCM5352
Based on Reduced Instruction Set Architecture (RISC)
The BCM5532 family of processors is a next generation SoC architecture that combines the CPU, Wireless MAC (media access controller), Ethernet MAC onto one chip RISC (reduced instruction set computer)
MIPS is used Sony playstation for example.

## Slide 11: BCM5352
Next generation SoC (System on a Chip)
SoC: combines CPU + Wireless MAC + Ethernet MAC onto one chip
Flash memory
SDRAM
Wireless access (802.11)
Ethernet switch

## Slide 12: WRT54GL Block diagram
See next slide:
Also follow this model:
CPU
Storage
Input
Output

## Slide 14: Storage
On board storage is indeed a limitation when using WRT54GL in situation other than for which it is meant for.
WRT54GL has a flash memory (4 MB), a form of non-volatile storage commonly used in small devices, such as digital camera.
It also use SDRAM (Synchronous Dynamic Random Access Memory) soldered directly into the printed board. DIMM (Dual In-line Memory Module)

## Slide 15: Wireless and Ethernet networking
WRT54GL has a powerful networking architecture
It provides 5 port Ethernet switch that is broken down into two virtual LANs VLAN0 and VLAN1 (default)
Wireless interface is bridged by default to the Ethernet switch.
WiFi component is BCM2050, a 802.11b/g radio chipset.
It uses a diversity chip to balance signals between two built-in antenna.
WiFi radio connects to the CPU Wireless MAC on eth1 which is bridged to VLAN0 via br0 interface.
Ethernet switch controls EthernetLAN and Internet lights, whereas Power, DMZ, WLAN are controlled by GPIO port on the CPU
WAN port: plug in cable modem into this port,
  it will pull a DHCP (Dynamic Host Configuration Protocol) address from your ISP (Internet Service Provider).
  Since it belongs to VLAN1 it is separate from VLAN0 and the two are linked by WRT54Gl’s routing capabilities.
  Firewall prevents traffic from flowing from WAN to LAN network, traffic initiated by LAN to exit via WAN.

## Slide 16: What does WRT54GL do?
Creates a network between the wireless interface and the LAN ports known as br0.
Router address is 192.168.1.1 by default.
WLAN port (port 4).
Typically you will plug your cable modem into this port; this will pull the DHCP address from your ISP.
WAN and LAN are separate network linked by WRT54GL

## Slide 17: Embedded XINU
http://xinu.mscs.mu.edu/Main_Page
XINU ("XINU Is Not Unix", a recursive acronym) is a Unix-like operating system originally developed by Douglas Comer for instructional purposes at Purdue University in the 1980s.
Embedded XINU is a reimplementation of the original XINU operating system on the MIPS processor which is able to run on inexpensive wireless routers and is suitable for courses and research in the areas of Operating Systems, Hardware Systems, Embedded Systems, and Compilers.

## Slide 18: Embedded Xinu
To port Xinu to embedded MIPS/other platforms
ANSI-compliant C
Meant for educational purposes
This particular project is a collaboration between University at Buffalo and Marquette university.
Our Xinu port ar UB is built with the help of federal grant from National Science Foundation (NSF) grant.

## Slide 19: The Basic Hardware modifications

## Slide 20: The NSF-Supported Facility at UB

## Slide 22: Embedded XINU Code
http://xinu.mscs.mu.edu/
ls xinu_mips-1.0
AUTHORS README include loader system tty
LICENSE compile lib shell test uart
Above is the xinu kernel directory organization
See attached XINU directory structure and class diagram
We will develop programs into XINU kernel on linux server called nexos.cse.buffalo.edu
We will cross compile this kernel and load the firmware into WRT54GL (“upload”) and test it

## Slide 23: Common Firmware Environment (CFE)
The Common Firmware Environment (CFE) is the firmware developed by Broadcom for the BCM947xx SoC platform (among others). It is the first code that runs when the router boots and performs functions similar to Apple's Open Firmware:
Initializes the system
Sets up a basic environment in which code can run
Optionally provides a command line interface non-standard usage
Loads and executes a kernel image
So, in normal operation, a user will not see CFE working at all; it will load the Linksys kernel and send it on its merry way without hesitation. For us, however, CFE is crucial, because it provides us with the ability to load an image over the network using TFTP.

## Slide 24: CFE: http://melbourne.wireless.org.au/files/wrt54/cfe.pdf
On startup, CFE performs the following low-level initialization:
  Reset and ROM trap handler vectors
  CPU and FPU initialization
  L1 and L2 Cache initialization
  Multiprocessor initialization
  Memory controller initialization
  PCI and LDT bus configuration
  Environment variables
  Console device initialization
  Bootstrap device initialization
Certain information, such as the physical memory layout and other critical information, are stored by CFE and are made available to boot loaders and operating systems via CFE’s external API.
Once initialization has completed, CFE is ready to load programs from the bootstrap device (UART, Flash, ports etc.)

## Slide 27: Connecting WRT54GL
You have modified the connections, connected the server to wrt54gl
using serial cable. How will you make bacn end recognize the server machine?

## Slide 28: Basic Xinu Environment
Server machine
Front end router
Back end router

## Slide 29: Extended Xinu Environment

## Slide 30: WRT54GL
Detailed instruction: http://xinu.mscs.mu.edu/HOWTO:Modify_the_Linksys_hardware
You DO NOT have to do this. We already did it for you.
Our goal is to get you familiar with working in the Embedded Xinu environment
Some of the following slides are by a long-time teaching assistant Panya Chanawangsu

## Slide 31: Introduction to NEXOS Lab
Log on to timberlake
Connect to the NEXOS server: ssh nexos.cse.buffalo.edu
Change your password: passwd

## Slide 32: Some Technical Terms
Cross Compiler
Shell
Kernel

## Slide 33: Cross Compiler
General idea:
  Compile a program on machine A
  Run it on machine B where an OS is not supported
In our case, we build the XINU system on a local machine and upload the executable to the routers.

## Slide 34: Shell
User interface for the operating system
Access to the kernel
Other programs are called through shell
CLI (Command Line Interface)
GUI (Graphical User Interface) – not available in our system

## Slide 35: Kernel
Lowest level but the most important part of an operating system
Resource management
Bridge between software and hardware

## Slide 36: xinu_mips-1.0.2.tar.gz
Obtain the tarball from home directory cd /home
Copy the tarball to your directory cp xinu_mips-1.0.2.tar.gz ~
Go to your directory and untar the package cd ~ tar zxf xinu_mips-1.0.2.tar.gz

## Slide 37: Compiling
Go to xinu_mips-1.0.2 cd xinu_mips-1.0.2
View all the files and folders ls
Go to the compile folder cd compile
Compile all the source files make

## Slide 38: Connecting to a router
View available routers xinu-status
You need the file xinu.boot so stay in the compile folder mips-console router_name
For example, mips-console moiz

## Slide 40: Disconnecting from a router
You have to release the router once you are done using it.
Press ctrl + spacebar
And then q
Other students have the right to ask me to kill your connection if you are logged on to the same router for more than 15 minutes.

## Slide 41: Working with Xinu/Nexos
Lets look at the code and update the shell functions to get started with Xinu
Lets reverse engineer and understand the current xinu code.

## Slide 42: Using in XINU
To view all available commands help
To call a function function_name arg1 arg2 …

## Slide 43: Adding your own commands
See http://xinu.mscs.mu.edu/Shell
Write and save your source file in the shell directory
Follow the naming convention: xsh_commandName.c
For example, xsh_myTest.c
Hint: use xsh_test.c in the shell directory as a template.

## Slide 44: Parameters explained
ushort = unsigned short (0 to 65,535)
nargs holds the number of arguments
arg[0] is the command itself
arg[1] is the first argument, arg[2] is the second argument, etc.

## Slide 45: Adding your own commands (cont’d)
Update the command table in shell/shell.c { “myTest”, FALSE, xsh_myTest }
Update include/shell.h command xsh_myTest(ushort, ushort, ushort, ushort, char *[]);
Update compile/Makefile. Look for ”SHL =” and add your source file to the list xsh_myTest.c

## Slide 46: Some basic C commands
To print something in standard output, fprintf(stdout, “CSE524\n”); fprintf(stdout, “%s”, args[1]);
To convert a string to its integer equivalent, int x = atoi(args[1]);

## Slide 47: Adding your own commands (cont’d)
Now you are ready to compile your command. Change your directory to compile and type make
Connect to a router and try running your command. mips-console router_name
Now when you type help, you should see your command added to the list.

## Slide 48: Resources
XINU reference page:
http://www.cse.buffalo.edu/~bina/cse321/fall2017/xinu
XINU main page: how to deploy XINU
http://xinu.mscs.mu.edu/Main_Page