## Slide 1: Realtime System Fundamentals : Scheduling and Priority-based scheduling
B. Ramamurthy

## Slide 2: Realtime scheduling
We will realtime system scheduling as in:
  Earliest deadline scheduling (EDS)
    Starting deadline
    Completion deadline
    Dynamic priority scheduling
  Rate monotonic scheduling (RMS)
    Periodic tasks are prioritized by the frequency of repetition (high priority to tasks with shorter periods)
    Preemptive scheduling
    Fixed priority scheduling
    Schedulability according to RMS
    Σ(Ci/Ti) <= n(21/n-1)
  Cyclic executives (pre-scheduled)
    Concepts of cycle, slot and frame
    Repeated execution
    times

## Slide 3: Motivating Problem
You are building a realtime system PLTO to send on a mission to Pluto and beyond. Consider three periodic tasks t1, t2, and t3 with {cpu time, period} as {40, 100}, {75, 300} and {50, 200} respectively. Examine the schedulability of these tasks on a processor in the system PLTO. (This problem may be equally applicable to a system in a modern automobile.)

## Slide 4: Task State Diagram
Ready
Blocked
New
Run
Task admitted
Resources allocated
Dispatched; cpu allocated
Waiting for event
Event occurred
Task exit

## Slide 5: Deadline driven scheduling
Parameters: ready time, starting deadline, completion deadline, processing time, resource requirement, priority, preemptive or non-preemptive

## Slide 6: Deadline Scheduling (periodic tasks)
Process Arrival Time Execution Time Ending Deadline
A(1) 0 10 20
A(2) 20 10 40
A(3) 40 10 60
A(4) 60 10 80
A(5) 80 10 100
• • • •
• • • •
• • • •
B(1) 0 25 50
B(2) 50 25 100
• • • •
• • • •
• • • •

## Slide 7
deadline
A1 B1 A2 B1 A3 B2 A4 B2 A5 B2
A1 A2 B1 A3 A4 A5, B2
(missed)
A1
(missed)
A2 A3 A4
(missed)
A5, B2
B1 A2 A3 B2 A5
A1 A2 B1 A3 A4 A5, B2
A1 B1 A2 B1 A3 B2 A4 B2 A5
Fixed-priority scheduling;
A has priority
Fixed-priority scheduling;
B has priority
Earliest-deadline scheduling
using completion deadlines
B1

## Slide 8: Aperiodic Task set
Arrival Time Execution Time Starting Deadline
A 10 20 110
B 20 20 20
C 40 20 50
D 50 20 90
E 60 20 70
Use earliest deadline with unforced idle time

## Slide 9: Rate-monotonic scheduling
First proposed by Liu.
For RMS, the highest-priority task is the one with the shortest period, the
second highest-priority task is the one with the second shortest period, and so on.
Schedulability according to RMS
    Σ(Ci/Ti) <= n(21/n-1)

## Slide 10: Critical sections and Semaphores
When multiples tasks are executing there may be sections where only one task could execute at a given time: critical region or critical section
There may be resources which can be accessed only be one of the processes: critical resource
Semaphores can be used to ensure mutual exclusion to critical sections and critical resources

## Slide 11: Resources & Critical Resources
Shared resources: need mutual exclusion
Tasks cooperating to complete a job
Tasks contending to access a resource
Tasks synchronizing
Critical resources and critical region
A important synchronization and mutual exclusion primitive / resource is “semaphore”

## Slide 12: Pthread and mutex
1. #include <pthread.h>
2. Declare mutex variable global to the threads, functions
pthread_mutex_t mtx; // declare
3. pthread_mutex_init(&mtx, NULL); //initialize
4. Identify critical section within thread; use mutex to realize mutual exclusion
pthread_mutex_lock(&mtx);
// code for critical section
pthread_mutex_unlock(&mtx);
5. Destroy mutex before exiting the program;
pthread_mutex_destroy(&mtx);

## Slide 13: Priority Inversion
When we allow concurrent task to execute and with semaphore and mailboxes and other synchronization primitives, it is possible that a low priority task may come to block a high priority task. This situation is known as priority inversion.
What happened on Mars?

## Slide 14: Priority inversion (Priority: t1>t2>t3)
task3
task2
Critical
section
task1
time
0 1 2 3 4 5 6 7 8 9 10
blocked

## Slide 15: Problem: Priority inversion Solution1: Priority Inheritance
task3
task2
Critical
section
task1
time
0 1 2 3 4 5 6 7 8 9 10
blocked
Priority of t1
inherited
Task 2 delayed
Priority reverted
To t3

## Slide 16: Solution2:Priority Ceiling Protocol
CS | Used by | Priority Ceiling
S1 | t1,t2 | P(t1)
S2 | t1,t2,t3 | P(t1)
S3 | t3 | P(t3)
Critical
section
task1
time
0 1 2 3 4 5 6 7 8 9 10
task2
task3
Acquire S2
Attempt to
Acquire S1
Acquire S1
Acquire S1
Acquire S2
Release S1
Release S2
No way