## Slide 1: Set, Block, and Byte in Cache

## Slide 2: Block and Byte
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Byte
Address
00
01
10
11
Block
Index
000
001
010
011
100
101
110
111
Block
Address
Goal: take advantage of spatial locality.
Organize memory and cache in blocks
Each block contains multiple bytes
So how to figure out where data should be placed in the cache? We use block address and block index.

## Slide 3: Locating block and byte in the cache
Assume a cache with 2k blocks, each containing 2n bytes.
For a byte of data, we utilize its address in main memory to locate its position in cache
  -- k bits of the block index selects one of the 2k cache blocks.
  -- The lowest n bits are now a block offset that decides which of the 2n bytes in the cache block will store the data.
Prior example used a 22-block cache with 21 bytes per block. Thus, memory address 13 (1101) would be stored in byte 1 of cache block 2.
m-bit Address
k bits
(m-k-n) bits
n-bit Block
Offset
Tag
Block Index
4-bit Address
2 bits
1 bit
1-bit Block
Offset
1
10
1
block address: (m-n) bits

## Slide 4: Example
1
0
1
2
3
Index
Tag
Data
Valid
Address (4 bits)
=
Hit
2
Block offset
Mux
Data
8
8
8
1
10
Tag
Index (2 bits)

## Slide 5: Set and Block
In a set-associative cache
  -- The cache is divided into groups of blocks, called sets.
  -- Each memory address maps to exactly one set in the cache, but data may be placed in any block within that set.
If each set has 2x blocks, cache is an 2x-way associative cache.
Several possible organizations of an eight-block cache.
0
1
2
3
4
5
6
7
Set
0
1
2
3
Set
0
1
Set
1-way associativity
8 sets, 1 block each
2-way associativity
4 sets, 2 blocks each
4-way associativity
2 sets, 4 blocks each

## Slide 6: Locating a set associative block
How to determine where a memory address belongs in an associative cache?
If a cache has 2s sets and each block has 2n bytes, the memory address can be partitioned as follows.
Block Offset= Memory Address mod 2n
Block Address = Memory Address / 2n
Set Index = Block Address mod 2s
Address (m bits)
s
t=(m-s-n)
n
Tag
Set Index
Block
offset
block address: (m-n) bits

## Slide 7: Generality of set associative
1-way set associative cache is the same as a direct-mapped cache.
If a cache has 2k blocks, a 2k-way set associative cache would be the same as fully-associative cache.
0
1
2
3
4
5
6
7
Set
0
1
2
3
Set
0
1
Set
1-way
8 sets,
1 block each
2-way
4 sets,
2 blocks each
4-way
2 sets,
4 blocks each
0
Set
8-way
1 set,
8 blocks
direct mapped
fully associative
x = k - s

## Slide 8
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Byte
Address
00
01
10
11
Block
Index
000
001
010
011
100
101
110
111
Block
Address
Set
1-Way Set-Associative Cache

## Slide 9
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Byte
Address
0
1
Set
Index
000
001
010
011
100
101
110
111
Block
Address
2-Way Set-Associative Cache
Address (m bits)
s
t=(m-s-n)
n
Tag
Set Index
Block
offset
block address: (m-n) bits

## Slide 10
Tag
Data Block
V
=
Block
Offset
Tag
Set Index
t
s
n
HIT
Tag
Data Block
V
Data
Word
or Byte
=
t
2-Way Set-Associative Cache
0
1
11
11
10

## Slide 11
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Byte
Address
000
001
010
011
100
101
110
111
Block
Address
Fully Associative Cache

## Slide 12
Tag
Data Block
V
=
Block
Offset
Tag
t
n
HIT
Data
Word
or Byte
=
=
t
Fully Associative Cache
110
1
110
010
100

## Slide 13: Course Evaluation Incentive
I will reveal one question of the final exam (5-10 points) as an incentive, if (and when) the response rate of the course evaluation reaches 80% !!!
https://sunyub.smartevals.com/

## Slide 14: Thank You!