## Slide 1: CSE 341 Computer Organization Lecture 14 Processor : Single-Cycle Implementation 3
Prof. Lu Su
Compute Science & Engineering
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design
§4.3 Building a Datapath

## Slide 3: Review of R-type Instruction
Register-to-register instructions:
  -- op: opcode
  -- func: specifies a particular arithmetic operation
  -- rs, rt and rd: source and destination registers
  -- shamt: shift
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits

## Slide 4: Fetching Instruction
Instructions are stored in Instructions Memory(IM)
-- Assume IM cannot be written or changed during running.
Program Counter (PC) register holds the address of current instruction.
-- MIPS instructions are 32 bits (4bytes)
-- MIPS memory is byte addressable
-- PC should be incremented by 32/8=4
Read
address
Instruction
memory
Instruction
[31-0]
PC
Add
4

## Slide 5: Executing R-type instruction
Step1. Read an instruction from IM.
Step2. Specify source registers using rs and rt.
Step3. ALU performs desired operations.
Step4. Store output of ALU to designation register (specified by rd).
Read
address
Instruction
memory
Instruction
[31-0]
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
I [25 - 21]
I [20 - 16]
I [15 - 11]
Result
Zero
ALU
ALUOp
op | rs | rt | rd | shamt | func
31 26 | 21 | 16 | 11 | 6 | 5 0

## Slide 6: Review of I-type Instruction
I-type instructions: lw, sw and beq etc.
  -- rt: destination for lw, source for beq and sw.
  -- address :16-bit signed constant.
lw $t0, –4($sp)
sw $a0, 16($sp)
op | rs | rt | address
6 bits | 5 bits | 5 bits | 16 bits
100011 | 11101 | 01000 | 1111 1111 1111 1100
101011 | 11101 | 00100 | 0000 0000 0001 0000

## Slide 7: Data Memory for I-type
I-type instruction needs to access data memory
Two control signals (1 for enable):
-- MemRead: read data from memory
-- MemWrite: write data to memory
32-bit width for address bus and data bus
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead

## Slide 8: Modification for lw/sw(1)
Because R-type and I-type are executed on the same hardware, some modification is required.
Example instruction: lw $t0, –4($sp).
$sp (32-bit) is added to -4 (16-bit)
-- a sign-extension block is required
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read
address
Instruction
memory
Instruction
[31-0]
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp

## Slide 9: Sign-Extension Shortcut
How to convert a binary number represented in n bits to a number represented with more than n bits:
To add the 16-bit number to a 32-bit register, the
computer must convert that 16-bit number to its
32-bit equivalent.
Take the most significant bit from the smaller quantity—the sign bit—and replicate it to fill the new bits of the larger quantity. The old nonsign bits are simply copied into the right portion of the new word.

## Slide 11: Modification for lw/sw(2)
Example instruction: lw $t0, –4($sp).
For instructions like add/sub, inputs of ALU are from two registers; for lw/sw, inputs of ALU are from one register and one immediate value
-- a multiplexer controlled by ALUSrc is needed.
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read
address
Instruction
memory
Instruction
[31-0]
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp

## Slide 12: Modification for lw/sw(3)
Example instruction: lw $t0, –4($sp).
Register file’s “Write data” input can store either the ALU output for instructions like add, or the data memory output for lw.
-- A mux controlled by MemToReg is needed.
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read
address
Instruction
memory
Instruction
[31-0]
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp

## Slide 13: Modification for lw/sw(4)
Example instruction: lw $t0, –4($sp).
Destination register of lw is in rt ; destination register for instructions like add is rd.
-- Another mux controlled by RegDst is needed to select the destination register from either rt or rd.
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read
address
Instruction
memory
Instruction
[31-0]
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp

## Slide 14: Offset for branch instruction
Constant in branch instructions is not an address but an instruction offset from the current program counter to the desired address.
beq $at, $0, L
add $v1, $v0, $0
add $v1, $v1, $v1
j Somewhere
L: add $v1, $v0, $v0
Target address L is three instructions past the beq
-- address field is 0000 0000 0000 0011.
-- Actual memory offset is 4*3=12 bytes.
000100 | 00001 | 00000 | 0000 0000 0000 0011
op | rs | rt | address

## Slide 15: Executing branch instruction
Step1. Fetch the instruction, e.g. beq $at, $0, offset, from IM.
Step2. Read the source registers, $at and $0, from the register file.
Step3. Compare the values in $at and $0 by subtracting them in ALU
Step4. If the subtraction result is 0, PC is loaded with the target address as PC + 4 + (offset x 4); otherwise PC is incremented to PC + 4 to fetch the next instruction sequentially.

## Slide 16: Modification for branch instructions
4
Shift
left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read
address
Instruction
memory
Instruction
[31-0]
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp

## Slide 17: Full Datapath