## Slide 1: CSE 341 Computer Organization Lecture 15 Processor : Single-Cycle Implementation 4
Prof. Lu Su
Compute Science & Engineering
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: Control Unit Design
Right now we have not considered how to generate control signal.
A control unit is responsible for setting all the control signals
-- Its input is the 32-bit instruction word
-- Its outputs are the control signals for data path
Most of the control signals can be generated from op field in the binary encoding instruction.
Next we show the generating mechanism of control signals for different types of instructions.

## Slide 3: Datapath With Control

## Slide 4: Virtual Control Unit
Combine two control units into a virtual control unit.
  --needs 13 bits of inputs.
  --6 bits from op field, 6 bits from func field, 1 bit from zero output of the ALU.
Control unit has 10 bits of output (including the control signal for jump)
A little different from textbook

## Slide 5: R-type Instruction Path
R-type instructions include add, sub, and, or, and slt.
ALUOp is determined by instruction’s func field.

## Slide 6: lw Instruction Path
Example load instruction is lw $t0, –4($sp)
ALUOp is 010 (add) to compute the address

## Slide 7: sw Instruction Path
Example store instruction: sw $a0, 16($sp)
ALUOp is 010 (add) to compute the address

## Slide 8: beq Instruction Path
Example branch instruction: beq $at, $0, offset
ALUOp is 110 (subtract), to test for equality
4
Shift
left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read
address
Instruction
memory
Instruction
[31-0]
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
ALU’s Zero output indicates the equality

## Slide 9: Control Signal Table
ALUOp for R-type instructions depends on the instructions’ func field.
PCSrc should be set as 1 when the instruction is beq and the zero output of ALU is 1.

## Slide 10: J-type Format
J-type format: jump instruction.
Unlike branch instruction, the last field of jump instruction contains a word address instead of offset.
A 26-bit address field allows jump to any address from 0 to 228.
Byte Address !
Word Address !

## Slide 11: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
000010
address
31:26
25:0
Jump

## Slide 12: Pseudodirect Addressing
The jump address is the 26 bits of the instruction concatenated with the upper 4 bits of the PC, followed by 00.
PC31...PC28 AD26...AD01 0 0
1001 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 11
1001 0000 0000 0000 0000 0000 0000 1100

## Slide 13: Jump instructions
000010
address
31:26
25:0
Jump