## Slide 1: CSE 341 Computer Organization Lecture 17 Processor : Pipelining 1
Prof. Lu Su
Computer Science Engineering, UB
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: Task III
Single-cycle implementation:
-- All operations takes in one clock cycle
Multi-cycle implementation:
-- Fast operations take less time than slower ones
Pipelining
-- Overlap the execution of several instructions

## Slide 3: Example from Laundry
Three steps for one load of laundry
-- One washer (takes 30 minutes)
-- One drier (takes 40 minutes)
-- One “folder” (takes 20 minutes)
Totally 20+30+40=90 minutes for one load of laundry

## Slide 4: Sequential Way
A sequential way for 4 loads need 6 hours.
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Time

## Slide 5: Pipelining Way
Each load is started as soon as possible (overlap)
Such pipelining strategy leads to take 3.5 hours

## Slide 6: Some Observations on Pipelining
Pipelining doesn’t reduce latency of single load
Pipelining increase throughput of entire workload
Multiple tasks are operated simultaneously via the use of different resources
The speedup achieved by pipeline is reduced by extra time to “fill” and to “drain” the pipeline.
6 PM
7
8
9
Time
30
40
40
40
40
20

## Slide 7: Pipelining
A general-purpose optimization technique
Analogous to daily lives
-- Assembly lines
-- Fast food restaurants
Rely on utilizing idle resource
Can be used to accelerate instruction execution (processors)

## Slide 8: Instruction Execution Review
At most 5 steps for executing MIPS instruction
Not all instructions need all five steps.
Step | Name | Description
Instruction Fetch | IF | Read an instruction from memory.
Instruction Decode | ID | Read source registers and generate control signals.
Execute | EX | Compute an R-type result or a branch outcome.
Memory | MEM | Read or write the data memory.
Writeback | WB | Store a result in the destination register.
Instruction | Steps required |  |  |  | 
beq | IF | ID | EX |  | 
R-type | IF | ID | EX |  | WB
sw | IF | ID | EX | MEM | 
lw | IF | ID | EX | MEM | WB

## Slide 9: Single-Cycle Datapath
4
Shift
left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read
address
Instruction
memory
Instruction
[31-0]
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
2ns
2ns
2ns
1ns
1ns

## Slide 10: Single-cycle Review
All five steps occur in one clock cycle.
-- “lw” in the instruction set has five steps
-- Cycle time must be long to accommodate it
-- In prior examples, all instructions needs 8ns.
Each hardware element can only be used once per cycle
-- Separate memory and data memory for “lw” or “sw” (need to access memory twice)
-- Multiple adders are required. One for instruction increments (PC) in the IF. Another for computation (EX). Additionally, an extra adder is needed for branches

## Slide 11: Instruction Fetch (IF)
Example instruction: lw (ignore PC incrementing and branching).
In the IF step, instruction is read from memory.
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite

## Slide 12: Instruction Decode (ID)
In the ID step, source register is read from the register file.
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite

## Slide 13: Execute (EX)
In the EX step, effective memory address is computed by using the source register and the instruction’s constant field.
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite

## Slide 14: Memory (MEM)
In the MEM step, the data memory is read via the address computed by the ALU.
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite

## Slide 15: Writeback (WB)
In the WB step, the memory value is stored into the destination register.
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite

## Slide 16: What we can find…
Each execution step uses a different functional unit.
That means, the main units are idle for most of the 8ns cycle!
  -- Instruction memory is used for just 2ns at the start of the cycle.
  -- Registers are read once in ID (1ns), and written once in WB (1ns).
  -- ALU is used for 2ns near the middle of the cycle.
  -- Reading the data memory only takes 2ns.
A lot of idle hardware!

## Slide 17: Make those idle units work
We do not have to wait for the entire instruction to complete before we can re-use the functional units.
An example: Instruction memory is free in ID step
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Instruction Decode (ID)
Idle

## Slide 18: Decoding and Fetching Together
In that case, we can let processor fetch the next instruction while we’re decoding the first one.
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Read
address
Decode 1st instruction
Fetch 2nd

## Slide 19: Executing, Decoding and Fetching
Once the first instruction enters its Execute stage, we can go ahead and decode the second instruction.
And since the instruction memory is free again, so we can fetch the third instruction…
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Decode 2nd
Fetch 3rd
Execute 1st

## Slide 20: Making Pipelining Work
Based on this idea, the lw instructions can be pipelined via 5 stages.
-- Stages are: IF, ID, EX, MEM, and WB
-- Such arrangement can support executing 5 instructions simultaneously: one in each stage.
-- Each stage has its own functional units.
-- Each stage can execute in 2ns, similar to multi-cycle implementation

## Slide 21: 5-Stage Pipeline
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
ID
IF
EXE
MEM
WB
2ns
2ns
2ns
2ns

## Slide 22: Pipelining Loads
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
lw $t1, 8($sp) |  | IF | ID | EX | MEM | WB |  |  | 
lw $t2, 12($sp) |  |  | IF | ID | EX | MEM | WB |  | 
lw $t3, 16($sp) |  |  |  | IF | ID | EX | MEM | WB | 
lw $t4, 20($sp) |  |  |  |  | IF | ID | EX | MEM | WB
6 PM
7
8
9
Time
30
40
40
40
40
20

## Slide 23: Pipeline Diagram
Pipeline diagram shows the execution of a series of instructions.
-- Instruction sequence is shown vertically (top to bottom)
-- Clock cycles are shown horizontally (left to right)
-- Each instruction is divided into its component stages.
Overlapping of instructions is shown in the diagram.
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | MEM | WB |  |  | 
and $t1, $t2, $t3 |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | MEM | WB | 
add $sp, $sp, -4 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 24: Some Terminology
The pipeline depth is the number of stages: 5 in this case
In the first 4 cycles here, the pipeline is filling, since there are idle functional units.
In cycle 5, the pipeline is full. Five instructions are being executed simultaneously, no idle functional units.
In cycles 6-9, the pipeline is emptying.
filling
full
emptying
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | MEM | WB |  |  | 
and $t1, $t2, $t3 |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | MEM | WB | 
add $sp, $sp, -4 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 25: Single vs Multiple vs Pipelining

## Slide 26: Pipelining Performance
Execution time on ideal pipeline:
--Time to fill the pipeline + one cycle per instruction
--What is the execution time for N instructions?
Compare with other implementations:
-- eg. Single Cycle with 8ns clock period ?
How much faster is pipelining for N=1000 ?

## Slide 27: Pipelining other instruction types
For other types of instructions, eg. R-type instructions, it only require 4 stages: IF, ID, EX, and WB
-- MEM stage is not needed.
Some problems when we try to pipeline loads with R-type instructions…
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $sp, $sp, -4 | IF | ID | EX | WB |  |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | WB |  |  |  | 
lw $t0, 4($sp) |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | WB |  | 
lw $t1, 8($sp) |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 28: A Solution: Insert NOP Stages
Enforce uniformity
-- Make all instructions take 5 cycles with the same stages in the same order
-- Some stages will do nothing for some instructions
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $sp, $sp, -4 | IF | ID | EX | NOP | WB |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | NOP | WB |  |  | 
lw $t0, 4($sp) |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | NOP | WB | 
lw $t1, 8($sp) |  |  |  |  | IF | ID | EX | MEM | WB
R-type | IF | ID | EX | NOP | WB
store | IF | ID | EX | MEM | NOP
branch | IF | ID | EX | NOP | NOP