## Slide 1: CSE 341 Computer Organization Lecture 19 Processor : Pipelining 3
Prof. Lu Su
Computer Science Engineering, UB
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: Task III
Single-cycle implementation:
-- All operations takes in one clock cycle
Multi-cycle implementation:
-- Fast operations take less time than slower ones
Pipelining
-- Overlap the execution of several instructions

## Slide 3: Review of pipeline diagram
Above is an ideal code fragment.
  -- Each instruction needs a total of five cycles for execution.
  -- One instruction begins on every clock cycle for first five cycles.
  -- One instruction completes on each cycle from that time on.
  -- Each instruction is independent (completely operates on different registers).
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $8, 4($29) | IF | ID | EX | MEM | WB |  |  |  | 
sub $2, $4, $5 |  | IF | ID | EX | MEM | WB |  |  | 
and $9, $10, $11 |  |  | IF | ID | EX | MEM | WB |  | 
or $16, $17, $18 |  |  |  | IF | ID | EX | MEM | WB | 
add $13, $14, $0 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 4: Example with dependencies
sub $2, $1, $3
and $12, $2, $5
or $13, $6, $2
add $14, $2, $2
sw $15, 100($2)
Several dependencies in this code fragment.
-- The first instruction, SUB, stores a value into $2.
-- $2 is used as a source in the rest of the instructions.
Not a problem for the single/multi cycle datapaths.
-- Each instruction is executed completely before the next one begins.

## Slide 5: Data Hazards (1)
Two data hazards in the pipelined datapath.
  -- The AND reads register $2 in cycle 3. Since SUB hasn’t modified the register yet, this will be the old value of $2, not the new one.
  -- The OR instruction uses register $2 in cycle 4, again before it’s actually updated by SUB.
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
sub $2, $1, $3 | IF | ID | EX | MEM | WB |  |  |  | 
and $12, $2, $5 |  | IF | ID | EX | MEM | WB |  |  | 
or $13, $6, $2 |  |  | IF | ID | EX | MEM | WB |  | 
add $14, $2, $2 |  |  |  | IF | ID | EX | MEM | WB | 
sw $15, 100($2) |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 6: Data Hazards (2)
The ADD instruction is okay, because of the design of register file:
  -- Registers are written at the beginning of a clock cycle.
  -- The new value will be available by the end of that cycle.
The SW is no problem at all, since it reads $2 after the SUB finishes.
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
sub $2, $1, $3 | IF | ID | EX | MEM | WB |  |  |  | 
and $12, $2, $5 |  | IF | ID | EX | MEM | WB |  |  | 
or $13, $6, $2 |  |  | IF | ID | EX | MEM | WB |  | 
add $14, $2, $2 |  |  |  | IF | ID | EX | MEM | WB | 
sw $15, 100($2) |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 7: Dependency Arrows(1)
Arrows indicate the flow of data between instructions.
  -- The tails of the arrows show when register $2 is written.
  -- The heads of the arrows show when $2 is read.
Any arrow that points backwards in time represents a data hazard in our basic pipelined datapath. Here, hazards exist between instructions 1 & 2 and 1 & 3.

## Slide 8: Dependency Arrows(2)
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
sub $2, $1, $3
and $12, $2, $5
or $13, $6, $2
add $14, $2, $2
sw $15, 100($2)
Clock cycle
1 2 3 4 5 6 7 8 9

## Slide 9: Resolving Data Hazards (1)
Strategy 1:
Wait for the result to be available by stalling earlier pipeline stages

## Slide 10: Stalled Stages and Pipeline Bubbles
stalled stages
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I3 I3 I3 I4 I5
ID I1 I2 I2 I2 I2 I3 I4 I5
EX I1 nop nop nop I2 I3 I4 I5
MA I1 nop nop nop I2 I3 I4 I5
WB I1 nop nop nop I2 I3 I4 I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) r1 (r0) + 10 IF1 ID1 EX1 MA1 WB1
(I2) r4 (r1) + 17 IF2 ID2 ID2 ID2 ID2 EX2 MA2 WB2
(I3) IF3 IF3 IF3 IF3 ID3 EX3 MA3 WB3
(I4) IF4 ID4 EX4 MA4 WB4
(I5) IF5 ID5 EX5 MA5 WB5
Resource
Usage
nop  pipeline bubble

## Slide 11: Resolving Data Hazards (2)
Strategy 2:
Forward data as soon as possible after it is calculated to the earlier pipeline stage

## Slide 12: How to eliminate hazards(1)
In the example AND and OR instructions in the example should use the correct value for $2.
When is the data is actually produced and consumed?
-- SUB instruction produces its result in its EX stage, during cycle 3 in the diagram below.
  -- AND and OR need the new value of $2 in their EX stages, during clock cycles 4-5 here.
 | Clock cycle |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
sub $2, $1, $3 | IF | ID | EX | MEM | WB |  | 
and $12, $2, $5 |  | IF | ID | EX | MEM | WB | 
or $13, $6, $2 |  |  | IF | ID | EX | MEM | WB

## Slide 13: How to eliminate hazards(2)
The actual result $1 - $3 is computed in clock cycle 3, before it’s needed in cycles 4 and 5.
-- In general, we need to somehow bypass the writeback and register read stages when needed.
-- More specifically, We need to pass the ALU output from SUB directly to the AND and OR instructions, without going through the register file.
 | Clock cycle |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
sub $2, $1, $3 | IF | ID | EX | MEM | WB |  | 
and $12, $2, $5 |  | IF | ID | EX | MEM | WB | 
or $13, $6, $2 |  |  | IF | ID | EX | MEM | WB

## Slide 14: Forwarding
The ALU result generated in the EX stage is normally passed through the pipeline registers to the MEM and WB stages, before it is finally written to the register file.
Hence, we could just forward that value to subsequent instructions, to prevent data hazards.
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
sub $2, $1, $3
and $12, $2, $5
or $13, $6, $2
Clock cycle
1 2 3 4 5 6 7

## Slide 15: Outline of forwarding hardware
Forwarding unit selects correct ALU inputs for EX.
-- If there is no hazard, the ALU’s operands will come from the register file, just like before.
-- If there is a hazard, the operands will come from either the EX/MEM or MEM/WB pipeline registers.
ALU sources will be selected by two new multiplexers, with control signals ForwardA and ForwardB.
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
sub $2, $1, $3
and $12, $2, $5
or $13, $6, $2

## Slide 16: Datapath with Forwarding Muxes
ForwardA
Instruction
memory
Data
memory
1
0
PC
ALU
Registers
Rd
Rt
0
1
IF/ID
ID/EX
EX/MEM
MEM/WB
0
1
2
0
1
2
ForwardB

## Slide 17: How to Detect EX/MEM Hazard(1)
An EX/MEM hazard occurs between the instruction currently in its EX stage and the previous instruction if:
  The previous instruction will write to the register file, and
  The destination is one of the ALU source registers in the EX stage.
Data in a pipeline register can be referenced using a class-like syntax. For example, ID/EX.RegisterRt refers to the rt field stored in the ID/EX pipeline.
DM
Reg
Reg
IM
DM
Reg
Reg
IM
sub $2, $1, $3
and $12, $2, $5

## Slide 18: How to Detect EX/MEM Hazard (2)
First ALU source comes from pipeline register when necessary.
if (EX/MEM.RegWrite = 1
and EX/MEM.RegisterRd = ID/EX.RegisterRs)
then ForwardA = 2
The second ALU source is similar.
if (EX/MEM.RegWrite = 1
and EX/MEM.RegisterRd = ID/EX.RegisterRt)
then ForwardB = 2
DM
Reg
Reg
IM
DM
Reg
Reg
IM
sub $2, $1, $3
and $12, $2, $5

## Slide 19: Pipelined Datapath and Control

## Slide 20: How to Detect MEM/WB Hazard(1)
A MEM/WB hazard may occur between an instruction in the EX stage and the instruction from two cycles ago.
DM
Reg
Reg
IM
DM
Reg
Reg
IM
DM
Reg
Reg
IM
sub $2, $1, $3
and $12, $2, $5
or $13, $6, $2

## Slide 21: How to Detect MEM/WB Hazard(2)
A MEM/WB hazard may occur between an instruction in the EX stage and the instruction from two cycles ago.
Counter example: a register is updated twice in a row.
add $1, $2, $3
add $1, $1, $4
sub $5, $5, $1
Register $1 is written by both of the previous instructions, but only the most recent result (from the second ADD) should be forwarded.
EX/MEM Hazard

## Slide 22: How to Detect MEM/WB Hazard (2)
Here is an equation for detecting and handling MEM/WB hazards for the first ALU source.
if (MEM/WB.RegWrite = 1
and MEM/WB.RegisterRd = ID/EX.RegisterRs
and (EX/MEM.RegisterRd ≠ ID/EX.RegisterRs or EX/MEM.RegWrite = 0)
then ForwardA = 1
The second ALU operand is handled similarly.
if (MEM/WB.RegWrite = 1
and MEM/WB.RegisterRd = ID/EX.RegisterRt
and (EX/MEM.RegisterRd ≠ ID/EX.RegisterRt or EX/MEM.RegWrite = 0)
then ForwardB = 1

## Slide 23: Forwarding Unit
The forwarding unit has several control signals as inputs.
ID/EX.RegisterRs EX/MEM.RegisterRd MEM/WB.RegisterRd
ID/EX.RegisterRt EX/MEM.RegWrite MEM/WB.RegWrite
The fowarding unit outputs are selectors for the ForwardA and ForwardB multiplexers attached to the ALU. These outputs are generated from the inputs using the equations on the previous pages.

## Slide 24: Datapath with Forwarding Unit
ForwardA
Instruction
memory
Data
memory
1
0
PC
ALU
Registers
Rd
Rt
0
1
IF/ID
ID/EX
EX/MEM
MEM/WB
Rs
0
1
2
0
1
2
Forwarding
Unit
EX/MEM.RegisterRd
MEM/WB.RegisterRd
ForwardB
ID/EX.
RegisterRt
ID/EX.
RegisterRs

## Slide 25: Data hazards for store(1)
Two “easy” cases.
DM
Reg
Reg
IM
DM
Reg
Reg
IM
add $1, $2, $3
sw $1, 0($4)
DM
Reg
Reg
IM
DM
Reg
Reg
IM
add $1, $2, $3
sw $4, 0($1)
1
2
3
4
5
6
1
2
3
4
5
6

## Slide 26: Data hazards for store(2)
A harder case
In which cycle is
-- The load value available?
-- The store value needed?
DM
Reg
Reg
IM
DM
Reg
Reg
IM
lw $1, 0($2)
sw $1, 0($4)
1
2
3
4
5
6

## Slide 27: Extended Datapath for Load/Store Bypassing

## Slide 28: Summary
Most instructions of real codes are dependent upon others.
  -- This can lead to data hazards in our original pipelined datapath.
  -- Instructions can’t write back to the register file soon enough for the next two instructions to read.
Forwarding eliminates data hazards involving arithmetic instructions.
  -- The forwarding unit detects hazards by comparing the destination registers of previous instructions to the source registers of the current instruction.
  -- Hazards are avoided by grabbing results from the pipeline registers before they are written back to the register file.