## Slide 1: CSE 341 Computer Organization Lecture 22 Memory (1)
Prof. Lu Su
Computer Science Engineering, UB
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: Today’s Content in Big Picture
I/O device
SW
ch1
ch2
Ch3,4
Ch5
Ch6
Part-I Ch2
Part-II Ch3,4
Part-III Ch1,5,6

## Slide 3: Course Evaluation Incentive
Course evaluation ends on May 11.
Your suggestions and comments are important!
Everyone is busy in the final weeks, so…
I will reveal one question of the final exam (5-10 points) as an incentive, if (and when) the response rate of the course evaluation reaches 80% !!!

## Slide 4: Memory
We have shown how to make a fast processor.
Now we will learn how to supply the processor with enough data to keep it busy
-- Memory
Memory
CPU

## Slide 5: Fast and Large Memory?
Modern computers depend upon large and fast storage systems.
-- Large capacities for many applications: datacenter, mobile devices
-- Fast speed to keep up with pipelined CPUs
From the perspective of technology, system designer can get both fast and large storage systems; however, you also need to consider the budget.

## Slide 6: In Real World…
Storage | Speed | Cost | Capacity
Static RAM | Fastest | Expensive | Smallest
Dynamic RAM | Slow | Cheap | Large
Hard disks | Slowest | Cheapest | Largest
Storage | Delay | Cost/MB | Capacity
Static RAM | 1-10 cycles | ~$5 | 128KB-2MB
Dynamic RAM | 100-200 cycles | ~$0.10 | 128MB-4GB
Hard disks | 10,000,000 cycles | ~$0.0005 | 20GB-400GB
Random Access Memory (RAM)
allows data items to be read or written in almost the same amount of time irrespective of the physical location of data inside the memory.

## Slide 7: CPU-Memory Bottleneck
Memory
CPU
Performance of high-speed computers is usually
limited by memory bandwidth & latency
  Latency (time for a single access)
    Memory access time >> Processor cycle time
    Problematic
  Bandwidth (number of accesses per unit time)
    Increase the bus size, etc.
    Usually OK

## Slide 8: Processor-DRAM Gap (latency)
Time
µProc 60%/year
DRAM
7%/year
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance

## Slide 9
Small,
Fast Memory
(RF, SRAM)
capacity: Register << SRAM << DRAM
latency: Register << SRAM << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  if data Î fast memory  low latency access (SRAM)
  If data Ï fast memory  long latency access (DRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data
Memory Hierarchy

## Slide 10: Cache

## Slide 11
CPU Registers
100s Bytes
<10s ns
Cache
K Bytes
10-100 ns
1-0.1 cents/bit
Main Memory
M Bytes
200ns- 500ns
$.0001-.00001 cents /bit
Disk
G Bytes, 10 ms (10,000,000 ns)
10 - 10 cents/bit
-5
-6
Capacity
Access Time
Cost
Tape
infinite
sec-min
10
-8
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Xfer Unit
prog./compiler
1-8 bytes
cache cntl
8-128 bytes
OS
512-4K bytes
user/operator
Mbytes
Upper Level
Lower Level
faster
Larger
Levels of Memory Hierarchy

## Slide 12: Memory Hierarchy: Intel Haswell Mobile Processor (2013)
Let programs address a memory space that scales to the disk size, at a speed that is usually as fast as register access
Goal: Illusion of large, fast, cheap memory
Storage Components | Size | Latency
Registers | 1 KB | 1 cycle
L0 cache | 6 KB | 
L1 Instr/Data cache | 128 KB | 700 GB/sec
L2 cache | 1 MB | 200 GB/sec
L3 cache | 6 MB | 100 GB/sec
L4 cache | 128 MB | 40 GB/sec
Main memory | 1~16 GB | 10 GB/sec
Disk | 1~4 TB | 2000 MB/sec (SSD)
Nearline storage | Up to exabytes | 160 MB/sec

## Slide 13
Small/fast storage, e.g., registers
  Address usually specified in instruction
  Generally implemented directly as a register file
    but hardware might do things behind software’s back, e.g., stack management, register renaming
Larger/slower storage, e.g., main memory
  Address usually computed from values in register
  Generally implemented as a hardware-managed cache hierarchy
    hardware decides what is kept in fast memory
    but software may provide “hints”, e.g., don’t cache or prefetch
Management of Memory Hierarchy

## Slide 14: Cache
How to find a balance between fast and cheap memory?
Cache, a small amount of fast, expensive memory.
-- Between the processor and main memory
-- Keeps a copy of the most frequently used data
from the main memory.
In overall, cache increases memory access speed
-- Cache for the access to the most frequently used
data
-- Main memory for the access to the less frequently used data.

## Slide 15: Role of Cache
Lots of
dynamic RAM
A little static
RAM (cache)
CPU

## Slide 16: Locality
In practice, it is hard to figure out what data will be “most frequently accessed” before a program actually runs,
-- It is hard to know what to store into the cache
Fortunately , most programs exhibit locality,
-- Temporal locality: If a program accesses one memory address, it is likely that it will access the same address again.
-- Spatial locality: If a program accesses one memory address, it is likely that it will also access other nearby addresses.

## Slide 17: Temporal Locality for Instruction Access
An example of temporal locality is loop.
-- The loop body will be executed many times.
-- Computer will need to access those same few locations of the instruction memory repeatedly.
Loop: lw $t0, 0($s1)
add $t0, $t0, $s2
sw $t0, 0($s1)
addi $s1, $s1, -4
bne $s1, $0, Loop

## Slide 18: Temporal Locality for Data Access
Programs often access the same variables over and over, especially within loops.
We can keep those commonly-accessed variable in the registers, but in many cases it is not possible.
-- Limited number of registers.
-- Sometimes data must be kept in memory
sum = 0;
for (i = 0; i < MAX; i++)
sum = sum + f(i);

## Slide 19: Spatial Locality for Instruction Access
Nearly every program exhibits spatial locality
-- Instructions are usually executed in sequence
If an instruction at memory location i is executed then the instruction, at memory location i+4 may also be executed in a high chance.
sub $sp, $sp, 16
sw $ra, 0($sp)
sw $s0, 4($sp)
sw $a0, 8($sp)
sw $a1, 12($sp)

## Slide 20: Spatial Locality for Data Access
Programs often access data that is stored contiguously.
-- A good example is arrays
-- Another example is the individual fields of a record or object
employee.name = “Homer Simpson”;
employee.boss = “Mr. Burns”;
employee.age = 45;
sum = 0;
for (i = 0; i < MAX; i++)
sum = sum + a[i];

## Slide 21: How Cache Utilizes Temporal Locality
The first time the processor reads from an address in main memory, as well as storing that data to the cache.
-- The next time that same address is read, the copy of the data in the cache is used
-- First read is a little slower than before (why?), but subsequent reads are much faster.
Lots of
dynamic RAM
A little static
RAM (cache)
CPU

## Slide 22: How Cache Utilizes Spatial Locality
When the CPU reads location i from main memory, a copy of that data is placed in the cache.
Instead of just copying the contents of location i, several values are copied into the cache at once, such as from locations i through i + 3.
-- If the CPU later does need to read from locations i + 1, i + 2 or i + 3, it can access that data from the cache and not the main memory.
The initial load is slow, but we’re gambling on spatial locality and the chance that CPU will need the extra data.

## Slide 23: Cache Hit and Miss
Cache Hit: The cache contains the data that we’re looking for.
Cache Miss: The cache does not contain the requested data.
Two basic measurements of cache performance.
-- Hit rate is the percentage of memory accesses that are handled by the cache.
-- Miss rate (1 - hit rate)
Typical caches have a hit rate of 95% or higher

## Slide 24: A Simple Cache Design
Caches are divided into blocks.
-- Number of blocks is usually a power of 2.
-- Assume each block contains one byte.
000
001
010
011
100
101
110
111
Block
index
8-bit data

## Slide 25: Four Questions on Cache Design
1. When copying a block of data from main memory to
the cache, where exactly should we put it?
2. How can we tell if a word is already in the cache, or if
it has to be fetched from main memory first?
3. When the small cache memory fill up. How to replace
one of the existing blocks in the cache by a new block from main RAM?
4. How can write operations be handled by the memory
system?

## Slide 26
1. When copying a block of data from main memory to
the cache, where exactly should we put it?
2. How can we tell if a word is already in the cache, or if
it has to be fetched from main memory first?
3. When the small cache memory fill up. How to replace
one of the existing blocks in the cache by a new block from main RAM?
4. How can write operations be handled by the memory
system?

## Slide 27: Where Should We Put Data in the Cache? (1)
Direct-mapped: each main memory address maps to exactly one cache block.
If the cache contains 2k blocks, then the data at memory address i go to cache block index
i mod 2k
0
1
2
3
Index
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Memory
Address

## Slide 28: Where Should We Put Data in the Cache? (2)
An equivalent way is to look at the least significant k bits of the address.
Taking the least k bits of a binary value is the same as computing that value mod 2k.
00
01
10
11
Index
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Address

## Slide 29
1. When copying a block of data from main memory to
the cache, where exactly should we put it?
2. How can we tell if a word is already in the cache, or if
it has to be fetched from main memory first?
3. When the small cache memory fill up. How to replace
one of the existing blocks in the cache by a new block from main RAM?
4. How can write operations be handled by the memory
system?

## Slide 30: Adding Tags
Sometimes multiple addresses of main memory map to the same cache block.
We need to add tags to the cache, which supply the rest of the address bits to distinguish.
00
01
10
11
Index
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Tag
Data
00
11
01
01

## Slide 31: Valid Bit
When started, the cache is empty, so adding a valid bit is required for each cache block.
-- When the system is initialized, all the valid bits are set to 0.
-- When data is loaded into a particular cache block, the corresponding valid bit is set to 1.
00
01
10
11
Index
Tag
Data
00
11
01
01
00 + 00 = 0000
Invalid
Invalid
01 + 11 = 0111
Main memory
address in cache block
1
0
0
1
Valid
Bit

## Slide 32: A Cache Hit
When the CPU tries to read from memory, the address will be sent to a cache controller.
-- The lowest k bits of the address will index a block in the cache.
-- If the block is valid and the tag matches the upper (m - k) bits of the m-bit address, then that data will be sent to the CPU.

## Slide 33: A Cache Miss
Slower main memory access is needed for cache miss.
-- Stalling pipeline until data from main memory is fetched.
After reading data from main memory, copy it to cache
-- Lowest k bits of the address specify a cache block
-- Upper (m - k) address bits are stored as tag
-- Data from main memory is stored in the block’s data field.
-- Valid bit is set to 1.

## Slide 34
1. When copying a block of data from main memory to
the cache, where exactly should we put it?
2. How can we tell if a word is already in the cache, or if
it has to be fetched from main memory first?
3. When the small cache memory fill up. How to replace
one of the existing blocks in the cache by a new block from main RAM?
4. How can write operations be handled by the memory
system?

## Slide 35: What if the caches fills up
Least recently used replacement policy
-- Assumes that older data is less likely to be requested than newer data.
Already implicitly solved in previous slides
-- A miss causes a new block to be loaded into the cache, automatically overwriting any previously stored data.