## Slide 1: CSE 341 Computer Organization Lecture 3 ISA : Assembly Language 2
Prof. Lu Su
Computer Science & Engineering
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: Operations on memory
Recall that
--Arithmetic operation must be with registers
-- Memory is needed for some cases
MIPS provides load and store instructions to access memory
Load: transfer data from memory to register
Store: transfer data from register to memory

## Slide 3: Load and Store Word
Load and store word is popular in MIPS
1 word= 32 bits = 4 byte
Most programming languages support several 32-bit data types.
--- Integers, memory addresses, pointers, single-precision floating number
--- Unless otherwise stated, we’ll assume words are the basic unit of data.

## Slide 4: Load and Store Word (ctd.)
Load word instruction (lw)
lw $t0, 20($a0) # $t0 = Memory[$a0+20]
---$a0: stores the starting position of array a[]
--- 20: Offset
Store word instruction (sw)
sw $t0, 20($a0) # Memory[$a0+20] = $t0
Note!!! The above two ASM codes are NOT the accurate versions, we will revisit them later.
Notes: The constant in a data transfer instruction (8) is called the off set, and the
register added to form the address ($s3) is called the base register.

## Slide 5: Computing with Memory
When your computation contains memory-based data, you should:
1. Load the data from memory to register
2. Do computation, store result in register
3. Store result in register to memory if need
Arithmetic operands are always registers, not memory

## Slide 6: Question
Write the ASM for following c code:
char A[4] = {1, 2, 3, 4};
int result;
result = A[0] + A[1] + A[2] + A[3];

## Slide 7: Question
Write the ASM for following c code:
char A[4] = {1, 2, 3, 4};
int result;
result = A[0] + A[1] + A[2] + A[3];
# Assume a0 stores the starting address of A[];
lw $t0, 0($a0);
lw $t1,1($a0);
add $t0,$t0,$t1; # A[0]+A[1]
lw $t1,2($a0);
add $t0,$t0,$t1; #A[0]+A[1]+A[2]
lw $t1,3($a0);
add $t0,$t0,$t1; #A[0]+A[1]+A[2]+A[3]
Note the above codes are NOT the accurate version, we will revisit them later.

## Slide 8: Memory alignment (1)
Be careful when using lw and sw !
Assume an array of words with starting address 2000 (stored in $a0)
-- The first word is at address 2000
-- The second word is at address 2004, not 2001!
-- How to access the second word?
lw $t0, 4($a0) sw $t0, 4($a0)

## Slide 9: Memory alignment (2)
Memory is byte-addressable
A word occupies adjacent 4 entries of memory (1word = 4 bytes)
Alignment requirement in MIPS
-- 0,4,8,12… are valid word address (offset value)
-- 1,2,3,5,7… invalid word address (bus error)
Notes: Byte addressing refers to hardware architectures which support accessing individual bytes of data rather than only larger units called words, which would be word-addressable. Such computers are sometimes called byte machines[1] (in contrast to word machines).[2]

## Slide 10: Example
Compile A[12] = h + A[8]
Assume $s3 stores the starting address of A[], value of h is in $s2
lw $t0, 32($s3)
add $t0, $s2, $t0
sw $t0, 48($s3)
Do not write something such as:
add 48($s3), $s2, 32($s3)

## Slide 11: Revisit the prior examples
Load word instruction (lw)
lw $t0, 80($a0) # $t0 = Memory[$a0+20]
---$a0: stores the starting position of array a[]
---20: Offset
Store word instruction (sw)
sw $t0, 80($a0) # Memory[$a0+20] = $t0

## Slide 12: Revisit the prior question
Write the ASM for following c code:
char A[4] = {1, 2, 3, 4};
int result;
result = A[0] + A[1] + A[2] + A[3];
# Assume a0 stores the starting address of A[];
lw $t0, 0($a0);
lw $t1,4($a0);
add $t0,$t0,$t1; #A[0]+A[1]
lw $t1,8($a0);
add $t0,$t0,$t1; #A[0]+A[1]+A[2]
lw $t1,12($a0);
add $t0,$t0,$t1; #A[0]+A[1]+A[2]+A[3]

## Slide 13: Pseudo-instructions
Sometimes the MIPS instructions are not very expressive
addi $a0, $0, 2000 # load 2000 into $a0
add $a1, $t0, $0 # copy $t0 into $a1
MIPS support expressive pseudo-instructions
li $a0, 2000 # load 2000 into $a0
move $a1, $t0 # copy $t0 into $a1
Assemblers translates pseudo-instructions into “real” instructions.

## Slide 14: Control Flow
Usually instructions are executed sequentially.
Sometimes control signal alters the flow.
High-level language has two types of control
Conditional statements (if-else)
-- executes only if test expression is true
Loop (for, while)
-- executes some statements many times

## Slide 15: Conditional Statements
Double the absolute value at a0
v0 = a0;
if (v0 < 0)
v0 = -v0; // may not be executed
v1= v0 + v0;

## Slide 16: Loop
Sum the elements of array a0
v0 = 0;
t0 = 0;
while (t0 < 5) {
v0 = v0 + a0[t0];
t0++;
}
These two statements will be executed 5 times

## Slide 17: MIPS Control Instructions
MIPS provides three control-flow instructions
-- j: unconditional jumps
j Label # jump to Label
-- bne and beq: conditional branches
bne $a1, $a2, Label # if $a1!=$a2, go to label
-- slt and slti: set if less
slt $a1, $a2, $a3 # $a1=1 if $a2 < $a3
Notes: bne: branch on not equal
beq: branch on equal
slt: set on less than
slti: set less than immediate

## Slide 18: Pseudo-branches
Besides beq and bne, MIPS assembler provides other pseudo instructions for branch
blt $t0, $t1, L1 # Branch to L1 if $t0<$t1
ble $t0, $t1, L2 # Branch to L2 if $t0<=$t1
bgt $t0, $t1, L3 # Branch to L3 if $t0>$t1
bge $t0, $t1, L4 # Branch to L4 if $t0>=$t1
Immediate versions are also associated.
blti $t0, 1, L1 # Branch to L1 if $t0<1
Notes: bgt: branch greater than

## Slide 19: Implementing Pseudo-branches
Pseudo-branches can be implemented with slt.
blt $a0, $a1, L1 # Branch if $a0<$a1
slt $a2, $a0, $a1 # $a2=1 if $a0<$a1
bne $a2, $0, L1 # Branch to L1 if $a2!=0
You can also implement immediate version.

## Slide 20: Question
How to implement bgt and bge

## Slide 21: Question
How to implement bgt and bge
bgt $t0, $t1, L3 # Branch to L3 if $t0>$t1
add $t2, $0, $0 # Initialize $t2=0
slt $t2, $t1, $t0 # $t2=1 if $t1<$t0
bne $t2, $0, L3 # Branch to L3 if $t2!=0

## Slide 22: Question
How to implement bgt and bge
bge $t0, $t1, L4 # Branch to L4 if $t0>=$t1
add $t2, $0, $0 # Initialize $t2=0
slt $t2, $t1, $t0 # $t2=1 if $t1<$t0
bne $t2, $0, L4 # Branch to L4 if $t2!=0
beq $t1, $t0, L4 # Branch to L4 if $t1=$t0