## Slide 1: CSE 341 Computer Organization Lecture 5 ISA : Assembly Language 4
Prof. Lu Su
Computer Science & Engineering
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: More Complex Example

## Slide 3: More Complex Example
0000 0000 0000 0000 0000 0000 0000 1101
0000 0000 0000 0000 0000 0000 0000 0001
AND

## Slide 4: Function (Procedure)
Function (Procedure) structures the code
int main() {
t1 = sum(5, 7);
}
int sum(int a, int b) {
int c=0; c=a+b;
return c;
}

## Slide 5: How to Translate Function Call in MIPS ASM
Three necessary steps:
--1. Change the control flow
--2. Pass the arguments and return values
--3. Allocate and destroy the local variables
Approaches in MIPS:
-- Special instructions for calling functions.
-- Conventions for sharing registers
-- Use of stack

## Slide 6: How to Translate Function Call in MIPS ASM
Three necessary steps:
--1. Change the control flow
--2. Pass the arguments and return values
--3. Allocate and destroy the local variables
Approaches in MIPS:
-- Special instructions for calling functions.
-- Conventions for sharing registers
-- Use of stack

## Slide 7: Control Flow
When calls a function, the control flow of the main program changes twice
-- Call the function
-- Return from the function
Each time function is called, CPU needs to remember the correct return address

## Slide 8: Control Flow in MIPS
Call function: jal (jump-and-link)
jal sum # call function sum
-- jal saves the return address (address of the next instruction) in the $ra before jump to function.
-- PC (Program Counter) register contains the address of the current executing instruction.
-- jal actually save PC+4 in $ra
Return: jr (jump return)
jr $ra # return to main program
- jr jumps to the address stored in $ra

## Slide 9: Control Flow in MIPS
PC
main
call sum
1100
1110
sum
$ra

## Slide 10: How to Translate Function Call in MIPS ASM
Three necessary steps:
--1. Change the control flow
--2. Pass the arguments and return values
--3. Allocate and destroy the local variables
Approaches in MIPS:
-- Special instructions for calling functions.
-- Conventions for sharing registers
-- Use of stack

## Slide 11: Data Flow
int main() {
t1 = sum(5, 7);
}
int sum(int a, int b) {
int c=0; c=a+b;
return c;
}
Function accepts
arguments from the main program
Function produces return results

## Slide 12: Data Flow in MIPS
$a0 - $a3 store arguments
$v0 and $v1 store return results
$ra stores returned address
No “type-check” in MIPS
--Be careful on consistent type

## Slide 13: How to Translate Function Call in MIPS ASM
Three necessary steps:
--1. Change the control flow
--2. Pass the arguments and return values
--3. Allocate and destroy the local variables
Approaches in MIPS:
-- Special instructions for calling functions.
-- Conventions for sharing registers
-- Use of stack

## Slide 14: A Problem on Register
In MIPS, registers for function are limited
-$a0~$a3 for storing arguments
-$v0 and $v1 for storing return results
What can we do to store more values?
In addition, more registers are needed for multiple calling the same function to reserve and destroy the local variables.

## Slide 15: Spilling Registers
We can spill register to memory.
Stack is an ideal data structure
-- Reserved in main memory
-- Last-in-first-out queue
-- Address of top element is stored in $sp
-- The stack grows downward in terms of memory address

## Slide 16: Breakdown of Main Memory

## Slide 17: Example
//main.cpp int a = 0;
char *p1;
main() { int b; char s[] = “abc”; char *p2; char *p3 = “123456”; static int c =0; p1 = (char *)malloc(10); p2 = (char *)malloc(20); strcpy(p1, "123456"); }

## Slide 18: Example
//main.cpp int a = 0; // Static
char *p1; // an area adjacent to Static
main() { int b; // Stack char s[] = “abc”; // “abc” in Text char *p2; // Stack char *p3 = “123456”; //“123456” in the Text static int c =0； // Static p1 = (char *)malloc(10); // Heap (Dynamic) p2 = (char *)malloc(20); // Heap (Dynamic) strcpy(p1, "123456"); // “123456” in Text }
p3 and s are in the stack

## Slide 19: Example
abc
123456
s
p3

## Slide 20: Stack and Heap
Stack: -- Downward Addressing, last-in-first out
-- Continuous area in the main memory
-- Top of stack and maximum size is pre-defined
-- Overflow may occur
Heap: -- Upward Addressing
-- Discontinuous area in the memory (linked list),
-- Flexible, large size
Malloc/New: --Request space from heap
-- Free/Delete is a must
--memory leak

## Slide 21: Downward Addressing of Stack

## Slide 22: Heap

## Slide 23: Pushing (store local variables)
To push elements onto the stack:
-- Move $sp down to make room
-- Store the elements into stack
For example:
addi $sp, $sp, -8 # make room
sw $t1, 4($sp) # push data
sw $t2, 0($sp) # push data

## Slide 24: Accessing and Popping (destroying local variables)
Access the element in stack
lw $s0, 4($sp) # retrieve $t1
Pop (erase) the element in stack
addi $sp, $sp, 4 # pop $t2
Note that the popped data is
still in the memory.

## Slide 25: Convention for Caller and Callee
Stack can also be used to
-- save the value of registers before overwritten by a function call,
-- then restore them after the function completes.
By convention, caller is responsible for saving and restoring the following registers
$t0 ~ $t9, $a0~$a3, $v0~$v1
Callee is responsible for saving and restoring registers
$s0 ~ $s7, $ra

## Slide 26: Example

## Slide 27: Naming Conventions