## Slide 1: CSE 341 Computer Organization Lecture 6: Signed and Unsigned Numbers
Prof. Lu Su
Computer Science & Engineering, UB
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: Binary Numbers
In any number base, the value of ith digit d is:
d × Basei
Numbers are kept in computer hardware as a series of high and low electronic signals, and so they are considered base 2 numbers.(binary numbers)
A single digit of a binary number is called binary digits or bits.

## Slide 3: Numbering of Bits within a MIPS Word
Least significant bit: the rightmost bit in a MIPS word.
Most significant bit: the leftmost bit in a MIPS word.
Can represent 232 different 32-bit patterns.

## Slide 4: Unsigned Numbers
Let a word represent the numbers from 0 to 232-1(4,294,967,295ten):
32-bit binary numbers can be represented in terms of the bit value times a power of 2:
These positive numbers are called unsigned numbers.

## Slide 5: Signed Numbers
Two’s complement representation: leading 0s mean positive, and leading 1s mean negative.

## Slide 6: Binary to Decimal Conversion
Represent positive and negative 32-bit numbers:
Example:

## Slide 7: Useful shortuts
A quick way to negate a two’s complement binary
number:
Simply invert every 0 to 1 and every 1 to 0,
then add one to the result. This shortcut is based
on the observation that the sum of a number and its
inverted representation must be 111 . . . 111two,
which represents 1.
x + = -1  +1 = -x

## Slide 9: Decimal to Binary Conversion
First consider the general case of binary to decimal conversion. (no sign bits but may have fraction part)
For the integral part, assume there are n bits: xn-1,
xn-2,…, x1,x0(from left to right), we have:
  DI = xn-1·2n-1 + … + x1·21+ x0·20
For the fractional part, assume there are n bits: x1,
x2,…, xn(from left to right), we have:
Df = x1·2-1 + x2·2-2+… +xn·2-n

## Slide 10: Decimal to Binary Conversion
Convert the integral part of decimal to binary equivalent : ( )
1. Divide the decimal number by 2 and store
remainders in array.
2. Divide the quotient by 2.
3. Repeat step 2 until we get the quotient equal to
zero.
4. Equivalent binary number would be reverse of all
remainders of step 1.
(Adapted from https://www.geeksforgeeks.org/convert-decimal-fraction-binary-number/)

## Slide 11: Decimal to Binary Conversion
Convert the fractional part of decimal to binary equivalent : ( )
Assume the
1. Multiply the fractional decimal number by 2.
2. Integral part of resultant decimal number will be
first digit of fraction binary number.
3. Repeat step 1 using only fractional part of decimal
number and then step 2.
Combine both integral and fractional part of binary number.

## Slide 12: Decimal to Binary Conversion
Example: Convert 4.3125 to binary. (3 precision after decimal point)
Step1: Conversion of 4 to binary.
1. 4/2: remainder = 0; quotient = 2;
2. 2/2: remainder = 0; quotient = 1;
3. 1/2: remainder = 1; quotient = 0;
So integral part is 100.

## Slide 13: Decimal to Binary Conversion
Step2: Conversion of .3125 to binary.
1. 0.3125 * 2 = 0.625, integral part: 0;
2. 0.625 * 2 = 1.25, integral part: 1;
3. 0.25 * 2 = 0.5, integral part: 0;
4. 0.5 * 2 = 1, integral part: 1;
So fractional part is 0.0101.
Step3: 100 + 0.0101 = 100.0101.

## Slide 14: Binary to Hexadecimal and Back
Since base 16 is a power of 2, we can trivially convert by replacing each group of four binary digits by a single hexadecimal digit, and vice versa.

## Slide 15: Binary to Hexadecimal and Back
Example:

## Slide 16: Notation in C
Binary: C doesn’t support binary literals, but we can use ‘0b’ before the binary number in C++ 14.
Octal: ‘0’ before octal number.
Hexadecimal: ‘0x’ before hex number.
Decimal: no other notation.