## Slide 1: CSE 341 Computer Organization Lecture 7 ISA : Machine Language 1
Prof. Lu Su
Computer Science & Engineering

## Slide 2: Today’s Content in Big Picture
Computer Organization and Design (5th edition) by Patterson and Hennessy
I/O device
SW
ch1
ch2
Ch3,4
Ch5
Ch6
Part-I Ch2
Part-II Ch3,4
Part-III Ch1,5,6

## Slide 3: Task 2: From ASM to Machine
add $t0, $s1, $s2
Machine language
Assembly language
High-level Language(C/Java)
A=B+C
Compiler
Assembler
HW-level operation
000010001100100100000000100000

## Slide 4: ASM vs Machine Language
So far we’ve been using assembly language, some readability
-- Operations (e.g., add) and operands (e.g., $t0).
-- Branches/jumps use labels instead of addresses.
-- Many pseudo-instructions.
Programs must eventually be translated into machine language
-- Binary format, stored in memory and decoded by CPU.

## Slide 5: Stored-Program Concept
The words of a computer’s language are called instructions, and its vocabulary is called an instruction set.
Today’s computers are built on two key principles:
  1. Instructions are represented as numbers.
  2. Programs are stored in memory to be read or written, just like data.

## Slide 6: Breakdown of Main Memory

## Slide 7: MIPS Machine Language
MIPS machine language: is designed for easily decode.
-- Each instruction has the same 32-bits length
-- Only three different instruction formats

## Slide 8: Instruction Encoding Example

## Slide 9: R-type Format
R-type format: design for register-to-register arithmetic/logic instructions, like add, and
-- op: operation code (opcode)
-- rs, rt: 1st and 2nd source register
-- rd: destination register
-- shamt: for shift instruction
-- func: used with op to select functions

## Slide 10: Number for Register
Recall that register can be represented by decimal number: eg. $t8 is $24
In MIPS machine language, register name is encoded by 5-bit binary number: eg.11000 represents $t8

## Slide 11: Example for Add
add $t0, $s1, $s2
0 17 18 8 0 32
000000 10001 10010 01000 00000 100000

## Slide 12: Example for Add
add $t0, $s1, $s2
Memory
Register File
s1
s2
t0
17
18
8

## Slide 13: Review of Memory
CS: chip select, enable/disable signal (CS=1/0)
ADRS: The address of memory being accessed
WR=0, read phase,
OUT=data stored in the
address (ADRS)
WR=1, write phase, data
stored in the ADRS is replaced
by DATA

## Slide 14: Memory in the MIPS
Byte-addressable, each data entry is 8-bit
Width of address bus is k=32
- totally 232 entries
- total volume can reach 4GB

## Slide 15: Register File
A combination of multiple registers
2k x n Register file
-- Contains 2k n-bit Registers
-- Write=1, D data stored into D address
-- No enable signal for read
-- When supplying the inputs of A address and B address, output appears as A data and B data

## Slide 16: MIPS Register File
32 x 32 Register file
-- Contains 32 32-bit registers
-- Register is for most frequently used data and operation (instruction)
-- Memory is for less frequently used and large-size (>32-bit) data.
-- More register is “expensive” due to
area budget

## Slide 17: Example for Sub
sub $t0, $s1, $s2
0 17 18 8 0 34
000000 10001 10010 01000 00000 100010

## Slide 18: Example for And
and $t0, $s1, $s2

## Slide 19: Example for And
and $t0, $s1, $s2
0 17 18 8 0 24hex
000000 10001 10010 01000 00000 100100

## Slide 20: R-type Format for Shift
Shift instruction is slightly different
-- rs is always 010
-- rt: source register
-- rd: destination registe
-- shamt: for shift instruction
-- func: used with op to select functions

## Slide 21: Example for Shift
sll $t2, $s0, 4
0 0 16 10 4 0hex
000000 00000 10000 01010 00100 000000

## Slide 22: Example for Shift
srl $t2, $s0, 4

## Slide 23: Example for Shift
srl $t2, $s0, 4
0 0 16 10 4 02hex
000000 00000 10000 01010 00100 000010