## Slide 1: CSE 341 Computer Organization Lecture 8 ISA : Machine Language 2
Prof. Lu Su
Computer Science & Engineering

## Slide 2: I-type Format
I-type format: designed for load/store, branch and immediate instruction.
- rs: source register for load/store; for branch or immediate instruction, it is operand.
- rt: for branches, it is source register; for other three cases, it is destination register
- address: 16-bit, from (-32768)10 to (32767)10

## Slide 3: Example for load
lw $s1, 100($s2)
23hex 18 17 100
100011 10010 10001 00000 00001100100

## Slide 4: Example for store
sw $s1, 100($s2)

## Slide 5: Example for store
sw $s1, 100($s2)
2bhex 18 17 100
101011 10010 10001 00000 00001100100

## Slide 6: Example for addi
addi $s1, $s2, 100
8hex 18 17 100
001000 10010 10001 00000 00001100100

## Slide 7: Branch
For branch instruction, the last field (16-bit) is not address
Since all the instructions are stored in the memory, the last field of branch instruction is the offset from the address of current instruction (program counter (PC)) to the address of the targeted instruction.
PC-relative addressing: The MIPS address is actually relative to the address of the following instruction (PC+4) as opposed to the current instruction (PC).

## Slide 8: Example for branch
Word Offset !
(not byte offset)

## Slide 9: J-type Format
J-type format: jump instruction.
Unlike branch instruction, the last field of jump instruction contains a word address instead of offset.
A 26-bit address field allows jump to any address from 0 to 228.
Byte Address !
Word Address !

## Slide 10: Example for jump
j 100

## Slide 11: Example for jump
j 100
2hex 2510
000010 00000 00000 00000 00000 011001

## Slide 12: From Program to Computer Example 1

## Slide 13: From Program to Computer Example 2

## Slide 14: From Program to Computer Example 2

## Slide 15: MIPS Addressing Mode Summary
Multiple forms of addressing are generically called addressing modes.
The MIPS addressing modes are the following:
  1. Immediate addressing
  2. Register addressing
  3. Base or displacement addressing
  4. PC-relative addressing
  5. Pseudodirect addressing

## Slide 16: Immediate Addressing
The operand is a constant within the instruction itself

## Slide 17: Example for addi
addi $s1, $s2, 100
8hex 18 17 100
001000 10010 10001 00000 00001100100

## Slide 18: Register Addressing
The operand is a register

## Slide 19: Base or Displacement Addressing
The operand is at the memory location

## Slide 20: Example for store
sw $s1, 100($s2)
2bhex 18 17 100
101011 10010 10001 00000 00001100100
00000 10001000111

## Slide 21: PC-relative Addressing
The branch address is the sum of the PC and a constant in the instruction.

## Slide 22: Pseudodirect Addressing
The jump address is the 26 bits of the instruction concatenated with the upper bits of the PC

## Slide 23: Short Summary
Machine language: Binary representation of instr.:
--The format in which the machine actually executes them
MIPS machine language is designed to simplify processor implementation
-- Fixed length instructions
-- 3 instruction encodings: R-type, I-type, and J-type
-- Common operations fit in one instruction
-- Uncommon (e.g., long immediate) require more than one