## Slide 1: CSE 341 Computer Organization Lecture 9 ISA : Assembly Language 5
Prof. Lu Su
Computer Science & Engineering
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 2: Nested Procedures
Procedures that do not call others are called leaf procedures.
In practice, procedures may invoke other procedures, sometimes even themselves.
Nested Procedures: push all the other registers that must be preserved onto the stack.
  The caller pushes any argument registers ($a0–$a3) or temporary registers ($t0–$t9) that are needed after the call.
  The callee pushes the return address register $ra and any saved registers ($s0–$s7) used by the callee.
  Upon the return, the registers are restored from memory and the stack pointer is readjusted.

## Slide 3: Example

## Slide 7: Example (n=3)

## Slide 8
SP
ra(n=3)
a0=3

## Slide 9
a0=3
ra(n=3)
SP
ra(n=2)
a0=2

## Slide 10
a0=3
ra(n=3)
SP
ra(n=2)
a0=2
ra(n=1)
a0=1

## Slide 11
a0=3
ra(n=3)
SP
ra(n=2)
a0=2
ra(n=1)
a0=1
ra(n=0)
a0=0

## Slide 12: CSE 341 Computer Organization Lecture 9 ISA : Machine Language 3
Prof. Lu Su
Computer Science & Engineering
Slides adapted from Raheel Ahmad, Luis Ceze , Sangyeun Cho,
Howard Huang, Bruce Kim, Josep Torrellas, Bo Yuan, and Craig Zilles

## Slide 13: PC-relative Addressing
The branch address is the sum of the PC and a constant in the instruction.
1001 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0010

## Slide 14: Pseudodirect Addressing
The jump address is the 26 bits of the instruction concatenated with the upper 4 bits of the PC, followed by 00.
PC31...PC28 AD26...AD01 0 0
1001 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 11

## Slide 15: Short Summary
Machine language: Binary representation of instr.:
--The format in which the machine actually executes them
MIPS machine language is designed to simplify processor implementation
-- Fixed length instructions
-- 3 instruction encodings: R-type, I-type, and J-type
-- Common operations fit in one instruction
-- Uncommon (e.g., long immediate) require more than one

## Slide 16: “C” Program to Number

## Slide 17
A combination of machine language instructions, data, and information needed to place instructions properly in memory

## Slide 18: Linker

## Slide 19
Many compilers produce object modules directly
Static linking
Translation and Startup

## Slide 20
Most assembler instructions represent machine instructions one-to-one
Pseudoinstructions: figments of the assembler’s imagination
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assembler temporary
Assembler Pseudoinstructions

## Slide 21
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: describes the size and position of the other pieces of the object file.
  Text segment: translated machine language code.
  Static data segment: data allocated for the life of the program.
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code
Producing an Object File

## Slide 22
Produces an executable file
  Merges segments
  Determine the addresses of data and instruction labels.
  Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space
Linking Object Files

## Slide 23
Load from executable file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including $sp, $fp, $gp)
  6. Jump to startup routine
    Copies arguments to $a0, … and calls main
    When main returns, do exit syscall
Loading a Program

## Slide 24
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all (transitively) referenced libraries
  Automatically picks up new library versions
Dynamic Linking