## Slide 1: CSE 486/586 Distributed Systems The Internet in 2 Hours: The Second Hour
Steve Ko
Computer Sciences and Engineering
University at Buffalo

## Slide 2: Recap
The Internet
  A network of networks
  A case study as a distributed system
Protocol
  An agreement between multiple parties
  Syntax & semantics
Design a system
  Why, what, and how
The Internet
  Connecting by layering

## Slide 3: Layering: A Modular Approach
Sub-divide the problem
  Each layer relies on services from layer below
  Each layer exports services to layer above
Interface between layers defines interaction
  Hides implementation details
  Layers can change without disturbing other layers
“The” computer science approach
  ISA, OS, networking…
Link hardware
Host-to-host connectivity
Application-to-application channels
Application

## Slide 4: Challenges in Layering
What to put on top of physical networks?
Assumption (for the sake of the discussion):
  Packet switching (a conversation is divided into smaller units called packets).
Basic things for enabling a conversation between remote hosts:
  Addressing (where do I send a msg?)
  Routing (how do I reach that address?)
Most importantly, survivability
  Protection of a conversation as long as there’s a physical path between entities communicating and they are alive.
What are some of the threats that disrupt a conversation?
  Packet loss, out-of-order delivery, duplicate packets, etc.
Notes: Most people, when they first design and implement something, do not worry about failures. But in the end, that’s where the most amount of effort goes in.

## Slide 5: We Must Ask Ourselves…
In a conversation, there are two components involved
  Hosts
  Network
So, one more question: how do you decide who does what? More specifically, what would be a good network/host division of labor?
Addressing and routing?
  Yeah, probably in the network
What about conversation protection mechanisms?
  The network or hosts?

## Slide 6: So, How to Protect a Conversation?
Think about the following scenario
Hey!
The Internet
Hey!

## Slide 7: Two Approaches to Survivability
Approach 1: “stateful” network
  The network keeps the state information about conversations
Hey!
The Internet
OK; Bob is sending something to Alice.
I’d better keep another copy in case it gets lost…

## Slide 8: Two Approaches to Survivability
Approach 2: “stateless” network
  The ends keep the state information about conversations
Hey!
(and let me know if you receive this)
The Internet
(OK; Alice didn’t speak to me for a while. I’ll send it again.)

## Slide 9: Two Approaches to Survivability
Stateless networks’ principle: fate-sharing
  The conversation shares the same fate with the “ends.”
  “it is acceptable to lose the state information associated with an entity if, at the same time, the entity itself is lost.”
Advantages
  Fate-sharing protects against any number of intermediate network failures (what about replication?)
  Fate-sharing is much easier to engineer.
The result: a “best-effort” network
  The IP (Internet Protocol) layer doesn’t really provide anything other than “best-effort” delivery (i.e., addressing and routing).
  The end hosts provide conversation protection mechanisms.

## Slide 10: The Internet Protocol Suite
UDP
TCP
Data Link
Physical
Applications
The Hourglass Model
Waist
The waist facilitates interoperability
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…

## Slide 11: IP Suite: End Hosts vs. Routers
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 12: End-to-End Arguments
Helps resisting the tendency to put and hide complicated things in the lower layers
If a functionality must be implemented end-to-end, then don’t implement it in the network.
  Exception: when there are clear performance improvements
Laid out in “End-to-End Arguments in System Design” by J.H. Saltzer, D.P. Reed and D.D. Clark (optional reading)
A good rule of thumb in any system design, but still not something to follow blindly

## Slide 13: CSE 486/586 Administrivia
PA 1
  Please try it out right away and see how far you can get.
Please use Piazza; all announcements will go there.

## Slide 14: TCP/IP
IP “best-effort” network
  The network knows the source and the destination.
  A conversation is divided into packets.
  Makes the best effort to deliver packets
  Packet loss, corruption, out-of-order delivery, etc. could all happen.
TCP (Transmission Control Protocol)
  Handles the problems
  Implemented at the end hosts
source
destination
IP network
TCP
TCP

## Slide 15: OK; Let’s Think about It Together…
Is this always a good thing?
Is today’s Internet still stateless?

## Slide 16: TCP
An end-to-end protocol
Protects conversations
  Receiver is supposed to send an ack (acknowledgement) packet.
  Packet loss  retransmission
  Out-of-order delivery, duplicate packets  sequence numbers
  Packet corruption  checksum
Controls congestion
  The network might be over-utilized
  Prevents the network from collapsing (which was actually a concern in the late 80’s)
TCP is an abstraction: a reliable, byte-stream connection

## Slide 17: A (Very) Brief Overview of TCP
Three-way handshake to establish connection
  Host A sends a SYN (open) to the host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
Why 3-way instead of 2-way?
  Reachability
SYN
SYN ACK
ACK
Data
A
B
Data

## Slide 18: Retransmission
Timeout & retransmission to handle packet loss
Packet
Timeout
Packet
ACK
Timeout
Packet lost

## Slide 19: The Dark Side of TCP
There’s overhead associated.
  Connection establishment: 3-way handshake
  Packet loss: retransmission timeout
  Congestion control: doesn’t utilize full bandwidth
More importantly, some applications do not need these.
Examples?
So, enter UDP (User Datagram Protocol): exposes almost exactly what IP can give you.

## Slide 20: Why Would Anyone Use UDP?
Fine control over what data is sent and when
  As soon as an application process writes
  … UDP will package the data and send the packet
No delay for connection establishment
  UDP just blasts away without any formal preliminaries
  … which avoids introducing any unnecessary delays
No connection state
  No allocation of buffers, parameters, sequence #s, etc.
  … making it easier to handle many active clients at once
Small packet header overhead
  UDP header is only eight-bytes long

## Slide 21: Popular Applications That Use UDP
Multimedia streaming
  Retransmitting lost/corrupted packets is not worthwhile
  By the time the packet is retransmitted, it’s too late
  E.g., telephone calls, video conferencing, gaming
Simple query protocols like Domain Name System
  Overhead of connection establishment is overkill
  Easier to have the application retransmit if needed
  Will cover this in a separate lecture
“Address for www.cnn.com?”
“12.3.4.15”

## Slide 22: What Applications See
TCP
UDP
IP
Device Drivers
Network Interface
OS
App
Socket API

## Slide 23: Summary
What to put on top of physical networks?
  Layers providing survivability
Where to put functionalities?
  Fate-sharing & end-to-end arguments
  IP layer doesn’t provide much
  TCP handles most of the survivability issues
TCP & UDP: the two transport protocols of the Internet
What interface do applications see?
  Socket API
Next: An introduction to Android programming

## Slide 24: Acknowledgements
These slides contain material developed and copyrighted by
  Indranil Gupta at UIUC
  Mike Freedman and Jen Rexford at Princeton