## Slide 1: CSE 486/586 Distributed Systems Cache Coherence
Steve Ko
Computer Sciences and Engineering
University at Buffalo

## Slide 2: Storage to Memory
We’ve looked at storage consistency.
The same consistency models are equally applicable to memory.
  Think multiple threads accessing the same memory addresses
But a memory system can have another form of consistency mainly for managing caches. We’ll look at this today.
  In a multi-core system, there are many caches, and they need to be synchronized.

## Slide 3: Caching Basics: CPU-Memory Bottleneck
Memory
CPU
Performance of high-speed computers is usually
limited by memory bandwidth & latency
  Latency (time for a single access)
    Memory access time >> Processor cycle time
    Problematic
  Bandwidth (number of accesses per unit time)
    Increase the bus size, etc.
    Usually OK

## Slide 4: Physical Size Affects Latency
Small Memory
CPU
Big Memory
CPU
Signals have further to travel
Fan out to more locations

## Slide 5: Memory Hierarchy
Small,
Fast Memory
(RF, SRAM)
capacity: Register << SRAM << DRAM (cost)
latency: Register << SRAM << DRAM (size)
bandwidth: on-chip >> off-chip (delays)
On a data access:
  if data Î fast memory  low latency access (SRAM)
  If data Ï fast memory  long latency access (DRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data

## Slide 6: Inside a Cache
CACHE
Processor
Main
Memory
Address
Address
Data
Data
Address
Tag
Data Block
Data
Byte
Data
Byte
Data
Byte
Line
100
304
6848
copy of main
memory
location 100
copy of main
memory
location 101
416
Notes: Tag only needs enough bits to uniquely identify the block (jse)
Limited size  need a replacement algorithm

## Slide 7: Cache Read
Look at Processor Address, search cache tags to find match. Then either
Found in cache
a.k.a. HIT
Return copy
of data from
cache
Not in cache
a.k.a. MISS
Read block of data from
Main Memory
Wait …
Return data to processor
and update cache
(Use a replacement algorithm
to select a line to replace)
Notes: We’re not going to talk about replacement algorithms here.

## Slide 8: Cache Write
Cache hit:
  write through: write both cache & memory
  write back: write cache only, memory is written only when the entry is evicted
Cache miss:
  no write allocate: only write to main memory
  write allocate (aka fetch on write): fetch into cache
Common combinations:
  write through and no write allocate
  write back with write allocate

## Slide 9: Administrivia
PA3 grading still going on
This Friday, no recitation, undergrad office hours from 2 pm – 4 pm & general office hours from 4 pm – 5 pm

## Slide 10: Memory Coherence in SMPs
Suppose CPU-1 updates A to 200.
write-back: memory and cache-2 have stale values
write-through: cache-2 has a stale value
Do these stale values matter?
What kind of guarantee do you get?
cache-1
A 100
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 100
memory
A 100
Notes: It definitely violates our expectation that a cache and memory have the same value.
Not much guarantee

## Slide 11: Cache Coherence
A cache coherence protocol ensures that all writes by one processor are eventually visible to other processors
  i.e., updates are not lost
  You can consider this a hardware-based update propagation mechanism for distributed caches.
Hardware support is required such that
  only one processor at a time has write permission for a location
  no processor can load a stale copy of the location after a write

## Slide 12: Cache Coherence
A memory system is coherent if:
A read by a processor P to a location X that follows a write by P to X, with no writes of X by another processor occurring between the write and the read by P, always returns the value written by P.
A read by a processor to location X that follows a write by another processor to X returns the written value if the read and write are sufficiently separated in time and no other writes to X occur between the two accesses.
Writes to the same location are serialized; that is, two writes to the same location by any two processors are seen in the same order by all processors.
(Coherence provides per-location sequential consistency).

## Slide 13: One Design: Snoopy Cache
Cache controllers work together to maintain cache coherence.
Each cache controller snoops on the bus traffic and “do the right thing.”
cache-1
A 100
CPU-Memory bus
CPU-1
CPU-2
cache-2
A 100
memory
A 100

## Slide 14: Snoopy Cache Coherence Protocol
For a read operation, a cache line is shared across multiple caches.
For a write operation, a cache line is not shared.
Each cache line has a state:
  M (modified): the processor has written to it.
  S (shared): other caches have a copy as well.
  I (invalid): the data is no longer valid.
Writing to a cache line
  If it’s M, the cache controller does the write.
  If it is not M, it sends an invalidation request to other caches, switches the state to M, and does the write.
  Other cache controllers switch the state to I.
Reading a memory address
  If it’s a hit, read it.
  If it’s not a hit, read it from memory, and other cache controllers switch the state to S.

## Slide 15: Cache State Transition Diagram The MSI protocol
M
S
I
M: Modified
S: Shared
I: Invalid
Each cache line has state bits
Address tag
state
bits
Write miss
(P1 gets line from memory)
Other processor
intent to write (P1 writes back)
Read miss
(P1 gets line from memory)
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Cache state in processor P1
Other processor reads
(P1 writes back)

## Slide 16: Two Processor Example (Reading and writing the same cache line)
M
S
I
Write miss
Read
miss
P1 intent to write
P2 intent to write
P2 reads,
P1 writes back
P1 reads
or writes
P2 intent to write
P1
M
S
I
Write miss
Read
miss
P2 intent to write
P1 intent to write
P1 reads,
P2 writes back
P2 reads
or writes
P1 intent to write
P2
P1 reads
P1 writes
P2 reads
P2 writes
P1 writes
P2 writes
P1 reads
P1 writes

## Slide 17: Observation
If a line is in the M state then no other cache can have a copy of the line!
  Memory stays coherent, multiple differing copies cannot exist
M
S
I
Write miss
Other processor
intent to write
Read
miss
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Other processor reads
P1 writes back

## Slide 18: MESI: An Enhanced MSI protocol increased performance for private data
M
E
S
I
M: Modified Exclusive
E: Exclusive but unmodified
S: Shared
I: Invalid
Each cache line has a tag
Address tag
state
bits
Write miss
Other processor
intent to write
Read miss,
shared
Other processor
intent to write
P1 write
Read by any
processor
Other processor reads
P1 writes back
P1 read
P1 write
or read
Cache state in processor P1
P1 intent to write
Read miss, not shared
Other processor
reads
Other processor intent to write, P1 writes back
Notes: E: you know that you’re the only one that has a copy (read permission). This improves performance when it moves from E to S because with MSI, we need to wait until other caches acknowledge.

## Slide 19: Scalable Approach: Directories
Every memory block has associated directory information
  keeps track of copies of cached blocks and their states
  on a miss, find directory entry, look it up, and communicate only with the nodes that have copies if necessary
  in scalable networks, communication with directory and copies is through network transactions
Many alternatives for organizing directory information

## Slide 20: Basic Operation of Directory
• k processors.
• With each cache-block in memory: k presence-bits, 1 dirty-bit
• With each cache-block in cache: 1 valid bit, and 1 dirty (owner) bit
• Read from main memory by processor i:
  • If dirty-bit OFF then { read from main memory; turn p[i] ON; }
  • if dirty-bit ON then { recall line from dirty proc (downgrade cache state to shared); update memory; turn dirty-bit OFF; turn p[i] ON; supply recalled data to i;}
• Write to main memory by processor i:
  • If dirty-bit OFF then {send invalidations to all caches that have the block; turn dirty-bit ON; supply data to i; turn p[i] ON; ... }

## Slide 21: Directory Cache Protocol
Assumptions: Reliable network, FIFO message delivery between any given source-destination pair
CPU
Cache
Interconnection Network
Directory Controller
DRAM Bank
Directory Controller
DRAM Bank
CPU
Cache
CPU
Cache
CPU
Cache
CPU
Cache
CPU
Cache
Directory Controller
DRAM Bank
Directory Controller
DRAM Bank
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 22: Cache States
For each cache line, there are 4 possible states:
  C-invalid (= Nothing): The accessed data is not resident in the cache.
  C-shared (= Sh): The accessed data is resident in the cache, and possibly also cached at other sites. The data in memory is valid.
  C-modified (= Ex): The accessed data is exclusively resident in this cache, and has been modified. Memory does not have the most up-to-date data.
  C-transient (= Pending): The accessed data is in a transient state (for example, the site has just issued a protocol request, but has not received the corresponding protocol reply).
Notes: - common cases
- read miss to private (victim clean or dirty)
- write miss to private
- read miss to shared
- write miss to shared

## Slide 23: Home directory states
For each memory block, there are 4 possible states:
  R(dir): The memory block is shared by the sites specified in dir (dir is a set of sites). The data in memory is valid in this state. If dir is empty (i.e., dir = ε), the memory block is not cached by any site.
  W(id): The memory block is exclusively cached at site id, and has been modified at that site. Memory does not have the most up-to-date data.
  TR(dir): The memory block is in a transient state waiting for the acknowledgements to the invalidation requests that the home site has issued.
  TW(id): The memory block is in a transient state waiting for a block exclusively cached at site id (i.e., in C-modified state) to make the memory block at the home site up-to-date.
Notes: TR (transitioning out of R)
TW (transitioning out of W)

## Slide 24: Summary
Cache coherence
  Making sure that caches do not contain stale copies.
Snoopy cache coherence
  MSI
  MESI
Directory-based
  Uses a directory per memory bank

## Slide 25: Acknowledgements
These slides heavily contain material developed and copyright by
  Krste Asanovic (MIT/UCB)
  David Patterson (UCB)
And also by:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252