## Slide 1: CSE 490/590 Computer Architecture Synchronization and Consistency I
Steve Ko
Computer Sciences and Engineering
University at Buffalo

## Slide 2: Last time…
Multithreading executes instructions from different threads
Coarse-grained multithreading switches threads on cache misses
Most of the OoO superscalar units are idle.
SMT utilizes most of the circuitry already present.
Levels of multithreading
  OoO superscalar
  Fine-grained
  Coarse-grained
  Multiprocessing
  SMT

## Slide 3: A Producer-Consumer Example
The program is written assuming instructions are executed in order.
Producer posting Item x:
Load Rtail, (tail)
Store (Rtail), x
Rtail=Rtail+1
Store (tail), Rtail
Consumer:
Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store (head), Rhead
process(R)
Producer
Consumer
tail
head
Rtail
Rtail
Rhead
R
Problems?

## Slide 4: A Producer-Consumer Example continued
Producer posting Item x:
Load Rtail, (tail)
Store (Rtail), x
Rtail=Rtail+1
Store (tail), Rtail
Consumer:
Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store (head), Rhead
process(R)
Can the tail pointer get updated
before the item x is stored?
Programmer assumes that if 3 happens after 2, then 4 happens after 1.
Problem sequences are:
  2, 3, 4, 1
  4, 1, 2, 3
1
2
3
4

## Slide 5: Sequential Consistency A Memory Model
“ A system is sequentially consistent if the result of
any execution is the same as if the operations of all
the processors were executed in some sequential
order, and the operations of each individual processor
appear in the order specified by the program”
Leslie Lamport
Sequential Consistency =
arbitrary order-preserving interleaving
of memory references of sequential programs
M
P
P
P
P
P
P

## Slide 6: Sequential Consistency
Sequential concurrent tasks: T1, T2
Shared variables: X, Y (initially X = 0, Y = 10)
T1: T2:
  Store (X), 1 (X = 1) Load R1, (Y)
  Store (Y), 11 (Y = 11) Store (Y’), R1 (Y’= Y)
  Load R2, (X)
  Store (X’), R2 (X’= X)
what are the legitimate answers for X’ and Y’ ?
(X’,Y’)  {(1,11), (0,10), (1,10), (0,11)} ?

## Slide 7: Sequential Consistency
Sequential consistency imposes more memory ordering constraints than those imposed by uniprocessor program dependencies ( )
What are these in our example ?
T1: T2:
  Store (X), 1 (X = 1) Load R1, (Y)
  Store (Y), 11 (Y = 11) Store (Y’), R1 (Y’= Y)
  Load R2, (X)
  Store (X’), R2 (X’= X)
additional SC requirements
Does (can) a system with caches or out-of-order
execution capability provide a sequentially consistent
view of the memory ?
more on this later

## Slide 8: Multiple Consumer Example
Producer posting Item x:
Load Rtail, (tail)
Store (Rtail), x
Rtail=Rtail+1
Store (tail), Rtail
Consumer:
Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead=Rhead+1
Store (head), Rhead
process(R)
What is wrong with this code?
Critical section:
Needs to be executed atomically by one consumer  locks
tail
head
Producer
Rtail
Consumer
1
R
Rhead
Rtail
Consumer
2
R
Rhead
Rtail

## Slide 9: Locks or Semaphores E. W. Dijkstra, 1965
A semaphore is a non-negative integer, with the
following operations:
  P(s): if s>0, decrement s by 1, otherwise wait
  V(s): increment s by 1 and wake up one of
  the waiting processes
P’s and V’s must be executed atomically, i.e., without
  interruptions or
  interleaved accesses to s by other processors
initial value of s determines
the maximum no. of processes
in the critical section
Process i
  P(s)
  <critical section>
  V(s)

## Slide 10: Implementation of Semaphores
Semaphores (mutual exclusion) can be implemented
using ordinary Load and Store instructions in the
Sequential Consistency memory model. However,
protocols for mutual exclusion are difficult to design...
Simpler solution:
atomic read-modify-write instructions
Test&Set (m), R:
  R  M[m];
  if R==0 then
M[m] 1;
Swap (m), R:
  Rt  M[m];
  M[m] R;
  R  Rt;
Fetch&Add (m), RV, R:
  R  M[m];
  M[m] R + RV;
Examples: m is a memory location, R is a register

## Slide 11: CSE 490/590 Administrivia
Quiz 2 (Friday 4/8): After midterm until today
Project 1 regrading
  Email and talk to both me and Jangyoung
Project 2 revision up soon (with some clarification)
  Always email me and the TAs together for project-related questions
  5th (define-your-own) deadline this Wed

## Slide 12: Acknowledgements
These slides heavily contain material developed and copyright by
  Krste Asanovic (MIT/UCB)
  David Patterson (UCB)
And also by:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252